Router allows computer in a internal network to talk to each other and get out on the internet.
The first device that connect you to the internet is the modem, behind that is router, underneath a router u have firewall(protect ur network from hackers), behind that a switch: a switch is a splitter of internet signals. All of ur computer devices will be connected to the switch and the switch allow them to communicate to each other or to go out onto the internet. Another device that will be on your network will be wireless access point. The wireless access point allows wireless computers and devices to then connect to the network. So the computers connect to the wireless access point which connects to the switch or they communicate to other devices on the network or to the internet.

   imagine ur pc is connected to switch which is connected to a router ….
So if u have 20 pc, they all connected to the same switch, they all physically connected all to the same switch. What we can do in the computer world is within that switch we can split and put 10 of the computers logically onto one network and the other half logically onto another network. So even though the computers are physically connected into that one switch, logically they are not able to talk to each other.

Modem:All the communication going out to the internet, hits that dsl modem, it turns your ethernet signals, the protocols, the language you used on your internal network into a language that can be used on the internet. For e.g your dsl modem turns that network communication into a language that verizon or whatever telephone company will understand.Your modem can be for T1 conn, cable conn,Dsl conn, satellite internet connection.
All these interne connection requires a modem to connect to the internet.
DSL: digital subscriber line. You have a solid connection between ur modem and the central office. Unlike other internet connection that share the bandwidth to a central place that goes onto the internet. You have a dedicated line.So ur speed wont go down because all of your neighbors got onto the internet at the same time.DSL wont get anymore fast. Comcast, cable modem, fire optic modem are getting faster.
DSL is asynchronous data transfer which means u can download faster than u can upload.
If u have a web server or u have a business people used something called vpn to get into your network, then you need to send data out to the internet.
Cable interent has introduced a new technology docis 3.0 1060Mb download speed. The thing with cable conn, is used do need to share the bandwidth that go onto the internet with ppl.
Satellite conn, download speed 1.5Mb/s , upload speed is very bad. You can’t do any real time communication ,voice over ip, remotedesk.
Wireless network 4G by sprint and verizon. You get a wireless device that connects to their cell-tower.
Router:allows you to seperate different network. You are sharing internet connection bet multiple diff business in one building. If you become a tenant and they offer you internet connection as part of the service. All the tenants in the bldg must be sharing internet connection, they need to somehow seperate different tenants onto their own private network. So your intenet connection will spit out from the modem and that will go out to different routers for different tenants within the bldg. So every tenant will have their own router.

So each tenant, doesn’t matter how many computer they have on their own internal network, can go out of the router and go out to the internet.
 But they cannot get into one of the other people internal network.

Router are used to logically divide networks and is normally used for internet connections. So If you wanna use one internet connection and provide that internet connection to multiple tenant on the network. So you have one internet connection and multiple routers connected, so all of those networks can connect to the internet without worring about anyone hacking them.

Firewall: tries to prevent hackers to get into your network through the internet. Its part of a security function, nowdays they get very very complicated. Firewall prevent internet traffic that you dont wanna to have happen. Theres software firewall, ips there you have entire servers that runs network of firewall within your network.
If you have firewall it will nowdays will be built-in into your modem or into your router. What you should remember, if it’s built into your modem or router, and you turn your firewall on, it will block internet services for the entire network. So, if you dont want ppl to get to website for some reason, it use port 80. If you block port 80 in the firewall built either on your router or the modem, then nobody in the entire network will be able to get to a website. If use firewall either built in modem or router, it will have effects on the entire network and even have some unintended consequences.
VPN: so keeping firewalls, n keeping people out of your network from getting into your network from the internet . You also need people outside of your office to get into your local network. People use vpn for this. It allow ppl to connect to your internal network from anywhere in the world.
As far as computers or networking devices are concerned that computer is now inside of your network. So if somebody is sitting in china and it wants to print something in miwaki, they can connect to your network using vpn and hit print and something will printed out in miwaki. So somebody on vpn can connect to all the shared files, folders or printer, or any resources that are shared on the internal network they will be able to access. It works slowly for someone from oustide cuz of ( their interent speed, your internet speed, some problem). It does this through client-server architecture. So you have a server inside your network, its a logical server it’s called a vpn-endpoint. This endpoint have username and password for the people who are allowed to connect to the network using vpn. Then the client computer, you normally install client application that can connect to the vpn endpoint. You’ll pass credentials it will authenticate, if everything is okey then that vpn endpoint will allow that computer to be on the network.
Why I said that vpn endpoint is a logical server?
>>> back in the days, there used to be things called radius-server or servers that all they did is allow ppl to remote access to their network. These type of server-service is built into a device. If you have windows server that have this service built into it. You can simply turn in it on. You do not need additional device to make this happen. Many of the commercial routers that you buy have this service built into them. They already have vpn service build into them. If you go through configuration routine, you can use that. You dont have to buy another device.

Switch: the device that connect all of the devices onto the network together to talk to each other. This device is either called a hub or a switch. If you have hub on ur network , you need to pull it out and throw it in the trash. Hubs are obsolete. Your network is slow is probably bcoz u have a hub.
Difference between a hub and a switch is : a hub is dumb and a switch has a little bit of intelligence. A hub split the internet signals or the network signals to everybody equally.

It’s literally like a complicated cable splitter, you have a cable wire coming into your house, you plug it into your splitter, with 3,4 or eight diff conn that runs on 3,8 diff tv’s in your house.

Switch are smart, they understand how to transfer data properly so that the network runs efficiently. All your wired devices everything with a network cable at some point comes into your switch. As you see on the back of the switch you have ports. All the computers plug into this ports, one of these ports goes into your router. For small business, you can get switches upto 48 ports. You’ll also hear managed and unmanaged switches.
Unmanaged switch has a little bit of brain power, but everything in it is absolutely automatic into it, so you can’t configured in it.
A managed switch like you are dealing with bldg or businesses that maybe using 48 computers. The managed switch allows you to go into the switch and programme it to do certain things. Basically it allows you to tune the network to make it properly. It allows you to play with things like QoS and others.
If you want fastest communication between all your computer in your network, you need to make sure your computer is capable of giga-bit networking and your switch is capable of giga-bit networking. A lot of people are buying these computer with really fast networking card in them but they conneting it to old switches. So the switch of switch will never be able to match the speed of the computer.

Wireless Access point.
Now that you have all your wired devices talk to each other, all the computers on your network now talk to each other and go out on the internet. Now you have to deal with your wireless devices whether they are wireless printers, iphone or laptop. All these devices needs to be communicate with everything on the network. They do this with something called wireless access point. All WAP is it allow all wireless computers and devices to connect to the network, they have antenna or some not have. All the computers connects wirelessly connect to them and they have one cable that goes from that wireless access point into that switch. That is how all the wireless devices can then communicate with the wired devices and the wired devices can communicate with the wireless devices through a WAP.
There are Four standards for wireless access points
1st standard is 802.11 (A,B,G,N) I.e 802.11 A, 802.11 B ….
B is compatible with {B,G,N} and G is {B} and N{B,G,N}
A died.
G is 54Mb/s is a lot faster. B and G are compatible. So if you have B wireless card it can work on a G network. If you have g wireless card it can work on B network. But B is old, so you shouldn’t have on your network.
New standard is 802.11 N, 10 yrs ago. They have had something called pre n so the process to get a standard implemented, to get everybody to agree on a standard can take a long time. A lot of companies come up with pre n standard. So a lot of companies look at current draft of that standard is, before it’s actually accepted and then they create their devices around that. But shouldnt buy it cuz it was still a draft it was before the the standard was finalized. It allows a lot much area to be covered by the wireless network. They allow for real time video and voice communication like VoIP, Skype, googleTalk.

Patch panel

SWITCH

Patch cable, goes from patch panel into switch

cables from your computer are connected to the back of the patchpanel.
Why use patch panel?
You know u gonna be moving ppl around the bldg or ppl might be in one location on next year, they are not there now. So what you do run cabling wherever you might need wired connection. Then you can connect those to the patch panel but u dont have to actually connect them to the switch. You can have in your bldg 200 network connection, they all are run, so if somebody needs a network connection they can plug into it. But you only have 48 ports switch. So you connect all those network cable that need to be live at the moment.
 So if your desk is here, you make sure that port is live, that port is connected to the switch at the patch panel.

Then you move ur desk over here, you might use a different network connection and you make that one alive.You take the connection that used before and the connect the new1 conn cable where it was.

Devices, client , server :
 Everything that is on the network is called a networking device, whether it’s a router or VoIP phone or computer..
In your business, you have a server if nothing else you have a file server, so u have one central computer that stores all files that everybody access over the network. All server is a network device that provides something to the rest of the network. So If u have shared printer, u have print server. So if u have shared files, so you have file server. A server provide services to other computers on the network.
Windows server are type of os creaed by Ms, these are very specific type of Operating system that provide specific type of function.
A client is any devices on the network that get services from a server.
Your computer you sit at, if you send a print job to a printer that is shared on another computer, you are a client of that computer. If you access a file, stored on another computer, you are a client of that computer. For ms its microsoft server 2008,2003, NT and they do very specific things.
Physical vs logical
physical is actual device, that u can pickup.
Logical:is how all actually works, so many devices can be connected to one switch, but they can be logically divided into seperate networks.
Nowdays the router you by have all built into it.
-----------

Understanding broadband technologies.
Ethernet, t1 lines, dsl , cable modem are used for data.
Synchronous or Asynchronous transfer:
Both cable and dsl are asynchronous, asynchronous means that the download speed is not the same as the upload speed.
Synchronous internet connection, these are t1, commercial or ethernet services are synchronous that they download and upload speed are the same.
Speed is how fast data gets push to your computer.
Latency is the time taken when you send a command to a web server to smthg on the internet and that cmd gets acknowledge and come backs to you.
So, if u say I wanna see a video on a website, when the video comes down. It maybe very fast. Latency is the moment you ask the video till you start getting them. For real time communication, you need latency very very low.
There are different class of service when you buy a broadband connection, you have business class service and you have residential client service.
Basically your ISP your verizon,comcast,quest. They really want business customers, business customers is where money’s at. Cuz business have their own internal tech support, isp gonna get less calls.

So, if you are getting internet service for your business, make sure it’s business class service. Better packages. They isp tech support respond quickly.
Ip address designate who u r on the internet.Everything on the internet needs an ip address. There are two types of ip addresses you can get when you get your broadband service. You can either get a static ip address or dynamic ip address.
A static ip address: This means that the computer will use this address to get to your network from the internet. So if you have a web server, they would go to this specific internet address. So if you have a web server or you use something called VPN or if you have anything on your network that ppl from the internet need to get to that resource you should have a static ip address.
Dyamic ip address: The little modem you have, it changes In a set period of time. Dynamic ip address means your ip address change whenever your ISP decide it should.
Two problems: 1. your ip address change, so if you have ppl trying to get into smthg in your network. 2. In email, a lot of spam filters block whenever smthg is coming from a dynamic ip address.
So if you setup a server and it has a dynamic ip address, when you go and send out emails, the spam filter see that the email came from one of the dynamic ip addresses and you will be blocked.
Use static ip address, people can get to your internal network pretty easily.

Port and services.
Every programme that uses the internet, uses a different port number, when you browse the web. You use port 80. when you use email you use smtp port. When you use remote control you use a different port. Your isp may block certain ports, so if you are trying to setup a web server for your website. Most residential internet connectios will block the port that you use to run the web server so if you use Verizon residential Dsl that web server wont work because will now allow the traffic that come into your web server. So contact your isp to know what ports are blocked. Most companies dont block any ports anymore some do.

Service Level Agreement: the service provider you dealing with, absolutely agrees how the service should be. So when you buy Comcast internet service or you buy verizon internet service, some down and some up.

They will tell you what you should get from your internet connection. But you might not always get it. Frankly we wont tell you the percentage of time you get the advertized speed. You dont have a SLA between them.
When you get T1 or carrier class ethernet conn, you get 99.99 % of uptime gurantee with the speed you purchased.
In past, the connection your house or business had was never really that fast. So many companies out there, could easily run website and the website could very easily keep up with the incoming traffic.even though they got 1K hits, for all that ppl, the speed was never really that fast. Now u have residential client and businees client. Cuz sometimes slowness is not your computer and not your internet connection, its the website internet connection.

Internet Connection:
T1(1.5Mb up and down)(sla)( they can go to places comcast and dsl cant go to)( This t1 line can be used for voice and data)( A t1 line consist of 24,64 bit channels) every 64 bits channel or kb/s channel can be used for data or for one telephone line. So even though they may have a t1 line but they may be using lets say 10 channels for 10 telephone lines, so instead of having 1.5 mb/s up and down they all may have 700Kb/s up or down. So they are using a number of the channels with that t1 line for voice instead of data. In order to get 1.5 Mb/s you have to use all 24, 64 bit channels. Each one of those channels can be used for either voice or data not both at the same time. So if the company that you are walking into if they use some no of channels for telephone line, then the speed they may have, may not be as fast.
Carrier grade africa: business class service(sla),synchronous data transfer.
(10mb up and down)
Point to point wireless
They have a tower, they place at a antenna on your bldg. It goes through the antenna. Latency is very good.
 The antenna have to be pointed at eachother for this. It’s directional. Nice speed. These type of internet conn isn’t provided by big tech giants. So service may not be good.

Wireless wireless service like 3G, WiMAX 4G edge

DSL is only ever offered by telephone companies. Its asynchronous conn. DSL Companies like verizon, quest,at&t can only put dsl service on their telephone lines. DSL is restricted by the distance from where your office is to the central office(is where all your telephone lines connect to in the telephone sys). Basically dsl singal travels down the telephone line it degrades to a point its no-longer useful. You have a dedicated line to the central office. For cable internet, every buddy in your area share that mainline, so if everybody gets on the internet. Your service will be slower.
Cable internet connection: comcast. The cable that goes to your tv split that and the cable that goes through your tv go to your cable modem.
DOCIS 3.0 Standard. Very good. Here if your neighbour used internet there will be reduction in speed. All this computer use smthg called a trunk line to go all the way to comcast.(no sla)

FIOS (fibre optic internet connection)

----
Physical network segmentation

This is how your network is physically divided up, when you build it out.
Ppl forget how you physically layout a network, how you run cables from point A to point B.
Dmark points: These are where authority for system transfer from one point to another. MDF and IDF, these are very important facility in your networking scheme. We gonna talk about Dmz (Demilitarzied zone).

Demarc: is the actual place where the authority or responsibility for a network transfers from one party to the next. You gonna see the most, the demarcation point for telephone company or for your ISP.
The telephone company or isp is only responsible for the internet connection all the way up to your bldg, once it’s inside your bldg. It’s your responsibility to deal with the network.
First dmarc point, is your telephone company or isp dmarc point, it will be situated near the entrance of your bldg. A grey telephone box that is verizon dmarc point. Verizon is responsible for data and telephone signals all the way up to that grey box. It has a prompt saying its verizon problem or its your problem. Dmarc point for telephone company is that little grey box. If you go out to that box and if you can get strong signal, that indicate the problem has to do smthg going on inside the bldg. If you not get telephone signal or dsl signal, then it’s say its verizon problem.

 The property manager may have their own cabling tha runs from isp dmarc to your offices. It will go all the way to ur MDF( the second Dmarc point). The dmarc point between u and the property manager is your property manager cable gets dump off into your office space.

The isp drops the cable off to the property management, the property management gives you a cable up to your office.
MDF(main distribution facility) and IDF(intermediary distribution facility)

 Lets say you renting 4 floor of this office bldg, so basically you have your property manager. Brings a cable to one of your floors and drops it off at a dmarc dmarc point. Where it drops off cable, it becames two things (1) It becomes a dmarc between you ad property manager, this is where everything transfer to your responsibility(2) Next thing it becomes a MDF( main distribution facility). Is literally where all the cables come back together to create the over-all network. So you basically have spider webs that create the network, this is one place where all connects back together. So normally when you dealing with small businesses, this is going to be the same place as your server room. You proabably have a server rack, switches, router, patch panel. Everything in the entire office or company is MDF. Once you start dealing with more complex infrastructure, MDF and the server room is not necessarily the same thing. The server room had to be much more secure than the MDF.
 This is the main central point where all network connection and
 telephone connection come back to. It’s the main hub of everything in your office.

So if you have a computer, you have to run it over the patch panel.
 You dont really wanna have a cable from your pc all the way to mdf, where patch panel is. So that’s where the concept of IDF came in (intermediary Distribution facility). So if you have office with multiple floors, so you have one mdf for the entire office and every single floor has its own idf.

 Lets u have all these computers here, lets say it has 100 pc, instead of having 100 network cables all the way to mdf, you run this cable all the way to idf. All the computers

all the telephone survillance sys would run to the idf for that floor. Each floor has its own idf and then the idf connects all the way to mdf. From each idf insead of running 100 cables, you are running 3 or 4 cables.

 This are called gbick connectors or normally they are called trunk connectors.

So basically all the computers on the floor will connect to the switch. A fire optic cable will connect to trunk connectors all the way to mdf. So one little gbick connection can handle traffic all the traffic for all this 48 ports.

DMZ ZONE( demilitarized zone):The final type of segmetation, isn’t so much a physical segmentation, this is smthg u could do logically. What this does is allow you to open up a portion of your network and internet connection that is more vulnerable to hackers than your core( more secure systems).
So you are running your own web server, many time are have to be more vulnerable to hacking than you want to active directory servers to be. Lets say you are running couple of web servers for your company. But on the same internet connection, you also have your internal network. So u have all hundred clients pc, active directory servers, email servers etc. Those web servers have to be more vulnerable cuz they have to be out there on the internet.
All you have to do to create a dmz, is basically you used two routers and two firewalls

So ur internet connection that will come to a router, so it could be ur isp:{comcast, verizon,quest}, this could be a t1 line, cable internet, dsl line,..
So that gonna come to this router into the firewall config. Now, since you have your web servers here, this firewall, this router config has to be as open you need it to be. So port 80, ftp port has to be open. Under the router you have a switch and this servers are hook to this switch and this servers are on the dmz, now there will be another connection that goes from ur switch to a more secure router. So u have one router here, this is very open and not secure cuz these allow ur web servers to get out onto the internet.

 then you have one connection from the switch that goes to your super secure router. This router say all the ports are complete lock down. You can say u only do email or web surfing.
On the other side of this, your entire internal network.
So basically all the dmz does is it gives you a space on your network that is less secure.

OSI MODEL : all OSI model is it’s just a logical model how network systems are supposed to communicate with each other. All the model does is breakdown different components of network and communication. Kinda slot them into layers.
So u make the physical layer, the physical layer is all the wiring, all the physical stuffs that connects computers together, then you have layer 2, the data link layer, this is the layer where switching occurs, all the switches that you plug your computer into, all what they do resides on the layer two. So basically the osi model is seven logicall layers, that allow you to think about networking problem and then figure out how to fix that problem. So if you understand how these layers work, then it’s much easier to focus on what the individual problem is, in the network system and then fix it. Programmers they do it the opposite way, instead of fixing things, they use the osi model to narrow in and figure out what exactly they have to build for.

OSI MODEL
- is made up of 7 layers, the layers from top to bottom are for what is closest to the end user( so whats user is interacting with), all the way down to shooting info down to the network.
 7Nth layer is Application layer: is the layer that the user is actually interacting with.(e.g firefox, IE ..)
6 layer is Presentation layer: this layer is the layer where the operating sys is on. So u interact with Application layer that sends info down to presentation layer, which is generally the layer, the layer that os works on.
5 layer is Session layer: the session layer that deals with the communication creating a session between the two computers. So if you are going to a website, basically your computer at the session layer has to create a session with the web server that you are trying to access to get the data from. The session layer actually creates a session between your computer and the computer you trying to get information from.
4 layer is Transport Layer: This layer decides how much info should be send at one time, so when you communicating with a website, this layer decides how much info you would communicate to the website, and how much info will be communicated back. This deals with transport of data, back and forth.
3 layer is the network layer: the layer router operates at, so your router u have in your home. So router operates at the network layer. So your ip address is at the network level.
2 layer is the data link layer: the data link layer is the layer at which switches operates on, so all the computers on the network gets plugged into the switch, so they can talk to each other. That layer is called data link layer.
1 layer is physical layer: is all the physical stuff that connects the computer together. This includes patch panel, patch cords, cabling etc.

So if your computer isn’t actually connected to the network, so if you dont have a patch cable running from your computer to the network then it’s a layer one problem, your network layer isn’t connected. If a cable gets cut or miswired that would be a physical layer problem that would be layer1 problem.
When you dealing with physical layer problems, physical layer is all the wiring and cabling, so if patch cable gets unplugged thats a physical layer problem. There’s no fancy config here, there’s no dos prompts, there’s no linux prompts, theres no fancy stuff. This is cat5 cable.

Above that is the data link layer, this is where switches resides, so we gonna have a class on switches to explain how all this works better. But basically this where things called MAC (Media Access Control) address reside. These addresses every single networking device in the world has an individual MAC address assigned to it. That is all part of the data link layer. Theres something called ARP (address resolution protocol), this is how switches work. Just understand everything about how switch operates resides on the data link layer, so that’s layer 2.you’ll hear term layer 2 switching. For later…
Above the data link layer is the network layer, this is where things called ip addresses reside. So anything that you do with the TCP ip protocol with ip addresses all of that happens at the network layer. So if you put in the wrong ip address and you cant get to wherever you want to get to, that is a network layer problem. If the router dies that is a network layer problem. Anything that involves your ip address would be a network layer problem.
Above this is transport layer: this has to do with something called windowing, windowing is a process where computers send info back and forth.Later..
Transport layer decides how large a block of information should be send, how long should the computer wait before it recieves any acknowledgment that info was sent or received.

Session layer: everytime a pc communicates with another computer, they have to open up a session, they have to be communicating with each other. So if you’re going to a banks website to look at your bank account info. When you go to that website you create a session between your computer and their computer, all that happens at the session layer.

Presentation layer: all you should really think about is the Operating system, so it’s a lot of configurable info but its not generally what the user is actually playing with, the user is normally up on the application layer.

Application layer problem: firefox is corrupted, some misconfig, etc.
Presentation layer: generally this is device drivers, something in the Os isnt allowing the user to go onto the internet. So they dont have the right security protocols, etc.

Session layer: So if you are dealing with a website if you administer a website you may have setting with your web server that are causing problems with the session layer, things like php config file, apache config files, if those arent setup properly your sessions may not be able to connect. So the user can get to your Web Server, they open a webpage on the web server. But the script that runs to open a session lets says to look at theirs bank account info, for some reason that isn’t working properly, that would be the session layer.

Network layer:
This is where router resides, you’re dealing with I say ip addresses, default gateway, subnet mask, dns. All that resides at network layer.

Data-link layer:
Anything you plugin the switch, the switches isn’t working properly, info isn’t being set properly. Sometimes the network is slow that can be a switching problem, ARP and mac addresses are at this layer.

When you walk into a situation you have no idea where to start, this tries to gice you just a model for about how to think about the problem, you walk in the entire server room is down or nobody can get onto the internet.
It could be email isn’t routing properly, thousands of ppl cant get to a web server that they need to get to, information isn’t sent properly.
The OSI models allows you to break down what the possible reasons could be and then go about fixing it.

So if ppl cant connect to a server, you go and see the back of the server and see the little connection light is lit. If lit that means you probably dont have a physical layer problem.

----
Understanding Switches
Switches run protocols, fancy cool stuff.

Switches are the core of your network, everything on your network connects to a switch at the end of the day. So if you install the wrong switch, you dont know how to trouble shoot switches, u have a problem.

Predecessor of switch is the hub.
A hub is a way to split ethernet signals the same way you have cable splitter in your house.
 The problem with a hub is this is genuinely a splitter, every communication that came into this hub was sent out to every single port that was on the hub. Basically a hub broadcast.
 The problem with that is simply, how the ethernet communicatio standards works, ethernet uses smthg called collison-avoidance and collision detection in order to sent packets. So basically ethernets sent info in packets. So in the figure, If pc-A wanna communicate with pc-B what it’ll do is listen to the network to see if anything is being communicated on the network. If nothing is being communicated on the network, it assumes that the network is available and it starts sending packets up to this hub and then the packets gets to the computer it trying to go to. But with the hub, you also trying to send this packets to every single other computer that is connected to the hub. First that ties up a lot of bandwidth. Lets say you have two computers that are trying to communicate with two other computers on the network. So pc-1 wanna talk to pc-3 and pc-2 wanna talk to pc-4.
So pc-1 and pc-2 gonna listen if theres any communication going on in the network. If there’s no communication on the network they gonna try to talk. So if pc-1 and pc-2 try to talk at the same time, so they gonna send packets at the same time, somewhere there will be a collision. So pc-1 and pc-2 packets gonna collide cuz only one pc can communicate at a time on a hub.
Ethernet std uses smthg called collision detection, so when that collision happens both pc-1 and pc-2 gonna hear that collision. They gonna wait a random amount of time and then try to start communicating again.
So lets say pc-1 will wait 3ms to send out a new packet.
pc-2 will wait 5ms to send out a new packet. So this time there will not ba collision hopefully.
The problem is as you start scaling up and you have more and more computers, all try to talk, these collisions starts to happening more and more often. This problem rise up to smthg called broadcast storm.
Lets say pc-1 tryna talk to pc-3, whats going to happen.
The first time the packets are going to be send to every single computer on the network. But this time the switches has some brains into it, the switch is then going to learn where pc-3 is. So when packets comes from pc-1, the switch goes, OoOo I see pc-1 is connected to port-1. So when it sends packets out, trying to send packets to pc-3. So when it sends packets out, to find pc-3, it broadcast the packets. pc-2 and pc-4 wont respond, cuz they dont care its not for them. Pc-3 will be like OoOo ty for those packets and it sends an acknowledgment. When it sends the acknowledgment the switch will be OoOo I see pc-3 is connected at port3. So in future pc-1 tries to communicate with pc-3, it will be like OoOo I see pc-3 is connected to port3. So now in future, instead of broadcasting out to all the ports on the switch, the switch will only send the packet to intended reciepent. So the switch starts learning where all the computers are connected to the switch.
Now this communication can be happening at the exact same time. So pc-1 maybe talking to pc-3 while pc-2 is doing a print job.

Switches resides at layer 2 of OSI model. The reason they reside at layer 2, is the way the switch learn which port, pc are connected. It does smthg called discovering the mac address of the device thats connected to it. Every single networking device have a mac address even switch,printers,routers(they have network card build intoit ). all network cards have mac addresses. So if u have laptop, the wireless card on that laptop have a mac address, also the hardwire RJ-45 plug also have a mac-address. All network working devices have mac addresses. All mac address are unique, the first half of the mac address is a identifier for the manufacturer of the equipment(Nortel,cisco,sus). The end of the mac address is like your social security no. so the switch figures out computer by their mac address. Will go later on mac address spoofing later.
Switches cares about the mac address of the device connecting to it.
The firstime, When the first pc tries to talk to another pc on the network, so first, when pc1 tries to talk to switch, the switch learns where that first pc is located and then switch broadcast the packets. When the destination pc responds, then the switch learns where that destination computer is.
Managed switches vs Unmanaged switches:
The idea behind managed versus unmanaged switches is how much you can configured the brain power inside the switch. In unmanaged switch is if it works it works, if it doesnt, rip that switch.
In managed switches, it allows you to set config. Basically a managed switch allows you to set those configuration, things like speed, duplex, vlans, Qos, class of service.
So If you pickup normal switch, you’ll see that all the switches will be 10/100 , what this means that they could either work at 10mb/s or 100mb/s.
Dealing with unmanaged switches, the switches will automatically detect what speed is coming through.
In managed switches you can do hardcoding that port to be 10mb/s or whatever.
Duplex: There is half duplex and full duplex, what it means that whether you can talk and listen at the same time. Half duplex can only talk or listen at any given moment.
If u having specific problem, lets say your server isn’t communicating very well, you can hardcode the port on your switch to be 100mb/s, full duplex.
Then you go to your server, you hardcode 100mb/s full duplex.

Back plane: is what connects all these ports together, each one of this ports are 100mb/s or 10mb/s. Backplane is what allows this ports to communicate with each other. The big thing that you just have to know when u go to buy a switch is what the total capacity of the backplane is. So basically all these computer tryna talk to eachother at the exact time, can the back plane ( the overall switch) can handle that communication.

Trunkports: if u wanna connect multiple switches together, u connect them together through the trunk port. When one computer tries to talk to another computer on the network, the switch will look to see that the computer is on the same switch. If not, it will send the data to the trunk port to go to the other switches that this switch is connected to.
So if you dealing with cisco and high end switches, this trunk port will be fios. In the video this gbick connection can actually handle 10Gb/s .
trunk port is a way of connecting multiple switches together.

VLAN( virtual local area networks) :
You can only setup a vlan on a managed switch or a high end switch, that you can go in and set configurations.
What vlans allow you to do, it allows you to seperate the ports in a switch into different networks.
Lets says you have multiple network cabling running back to one idf, but you dont want those network to talk, you want them to entirely seperate. This come into place nowdays with something called convergence, now that we are using VoIP telephones, we are using a survillance system, computers. We may not want those devices to talk to each other at all. We want them to put them on their own wall little garden, so they do not communicate. You dont want a virus to take down ur computer system, which has taken over your phone system.
So what vlans allow you to do, it allows you to seperate the ports, it allows you to seperate the ports into different virtual Lan, so the computers on vlan can not in any shape or form can talk to each other.
 Here , although they are connected to the same exact switch, bcoz you divided the different ports into different vlans, they can’t communicate to each other at all.

As far as everything is concerned, this are connected to entirely different systems. Something that confuses some people, well if this all r on the same physical device, can I get one vlan talk to the other vlan?
> Absolutely not.
The only way you can let one Vlan talk to another Vlan is if you actually put a router and connect one port from one vlan to another port on another vlan. Vlan get into something called convergence, once you start doing pc, telephone, survillance all on the same network.

Power over ethernet:
convergence is where you know use VoiP Telephones, use camera that are connected to the internet or network, things that do not used to be connected to the network are now connected to the network. Well somebody say hey, wouldnt it be nice to send power to all this little device using a switch instead of plugging the device in. so instead of running a power cable all the way to the survillance camera, you can power the survillance camera or telephone simply off the ethernet cable.
The switch sends data and power also. So u get 12.9 watts of power.
Cisco WAP would power over ethernet, its great.
So u either plug the WAP into power over ethernet switch or something called power over ethernet injector. So all you gotta do is run one cat5 cable to wherever you want your wap. So its connects to the network and is powered at the same time.
Always buy good quality stuff, cuz the problem is with some of the power over the ethernet there is a commununication routine between the switch and the device it tryna power. There are multiple standard for power over ethernet. So when you plug a device into a switch, the switch will ask what version are you, then the switch will send right amount of power.
The other thing is to realize with power over ethernet is, just like the back plane of the switch , that is the overall amount of communication that the switch can do it any1 time. A switch can use a maximum wattage at any one time.
So lets say you have 48 ports switch, it says it can pump out 13 watts per port. You have to look at the specs sheet, for how much total wattage they can put out. So lets say it can put out 130 watts, that means although you have 48 port switch, you can only connect 10 devices. You have to look at this on the specs sheet. So if you buy cisco power over ethernet device, how much power it can put out per port, then it can say how much power the entire device can put out. So even all 48 ports are powered over ethernet, the total load may not be able to support 48 ports power over ethernet. So your power runs through that cat5 cable.

QoS
Convergence is all the new and old technologies trying to use the internet.
Telephone system used to use only telephone cable. Now we have VoIP telephones, that use the network. Survillance camera used to use their own Coaxe cables, now they are using the network. With all this stuff trying to use the network, come into problems with communication. So basically if u r trying download a file, it doesnt really matter how fast or slow the file download as long as u get it, at the end of the day it’s ok. But when you’re dealing with VoIP, VoIP has to be very fast communication. What network manufacturers did, is come up with QoS and cisco calls it CoS(class).
Whenever you send data, you send that data into packets.packets are lowest unit of data, it has headers on it, it’s how something goes around.
What Qos or Cos does is, it prioritize packets based on what the packet is, so VoiP packet is consider a higher authority, then a live video stream packets.
At the end of the day, end users that are downloading email or swapping files, dont notice the difference, what it does, it make sure your entire bandwidth doesnt get bog down. So by Qos or Cos , you prioritize your packets.
Spanning Tree protocol
TCP/IP protocol protocol that we used for network communication.
IPX, SPX,.. network protocols that allow different computers to talk to each other.

Routing protocols:
router and switches has also have protocols that allow to communicate with each other.
All this highend switches and routers talk to each other using diff routing protocols there something called rip, open shortest path first, spanning tree protocol.

Spanning tree protocol: used by switches, it allows switches talk to each other and be able to route packets the fastest way possible between multiple switches. Best par is it prevents you from having something called router loops or routing loops.
So here’s my switch, if I put one cable from port1 to port2, what would happen is: what happens this switch when it tries to talk other pc on the network, it will start sending the signal through this, its called smthg a loop, the communication is put into a loop, that loops starts burning more processing power on the switch, in a min or two, ur network will get shutdown.

Lets say you have network jack in ur office, u have two network ports, ppl say hey I wanna connect a extra computer in my office, so they take a cable from one network jack and plug it into the switch, and then they plug their two pc. Good from here, but then
So then somebody who doesnt know what he is doing, plugs the cable to the other network jack and plugs that into new switch.

Use cisco router, cuz it uses spanning tree protocol.

Understanding soho routers
soho:- small office home office routers
nomral routers only basically do one thing, basically they route traffic between different subnets.(take tcp ip class). Basically a nomral router does is route traffic between different subnets.
A normal big routers does a lot of routing between different subnets.
For small office, you dont need all that power just to do routing, cuz u only got 4-5 computers on the office. What cisco, linkses, junipese is done, is they came up with soho routers, is they combine multiple logical device into a single device.
Cisco enterprise router all it does is route information between different subnets. But it routes a whole bunch of info between different subnets.
Soho routers doesnt deal with so much info, they have a lot of services in them ( vpn,firewall,switch, dhcp server,dns server)
SOHO vs Enterprise
Any network equipment are break into 3 classes: residential class( low,cheap), soho networking equipement(99.99%) less quality than,enterprise( 100% uptime).

All soho equipment is web gui administrable.
So bascially you go to web browser and you go to ip address of networking equipment, you can configure the networking equipement through web interface.
 For any enterprise stuff, you have to go to cisco cli, wer u have to type out dos like commands in a terminal prompt. Doing those dos like cmd are much more solid much more secure. But u and ur employee gonna have a much larger learning curve to deal with that.

When you have a business, theres a good chance you maybe hosting stuff on ur internal network, u may have a web server or ms small business server(ppl to get vpn access).

The best way to deal with external ip address is to deal with static ip address. As long as you have the service, this is the ip address that you have. All tcp/ip networking is based on the ip addresses.
A dynamic ip address changes once in a while. If ur ip address changes it cuz a havoc if ppl trying to get in. when ppl try to get to a email server they use a mx record,ww record, cname record, a record, etc.

 If you have a web server and if the dns is pointed toward this dynamic ip address and dynamic ip address changes, your web server goes offline.
All the traffic from the outside world, that is coming to your router or to your internal network, has to go to an ip address. If you have a static ip address it will always be the same, then you dont have to worry about changing your configurations.
When dealing with a router, is that the external port right here can either be configured for either dynamic ip address or for a static ip address.

DHCP
The first service that your soho router will provide for your network is DHCP. Every piece of networking equipment has an ip address. Considering pc, you can give them either static ip address this means you go to every single pc and you specificically state what ip address has so.
If you deal with a large network that is complete pain, so we have DHCP, so the router automatically assign ip address to the computers.
So whenever computer connects to a network it will ask for an ip address and the router will give it.

Remember, when dealing with a DHCP, that the router will give out the dhcp addresses from the pool that it has so basically within the configuration for your router you can state what range of ip address that you want the router to give out.
For 100 ppl: 192.168.1.100 – 192.168.1.200	(DHCP scope)
why this is very important, when you go to port fowarding, some devices on your network and server should always have a static ip address.
If u have 2 devices on the network with same ip address, sometime it goes to email server or sometimes goes to someother device or sometimes it goes to hell.
So u have to make sure this router isnt handing out ip address for computers that have static ip address.
Alot of times when you have small network, you let the router be dhcp server. Once you got a real servers on your network, you want those server to handle being a dhcp server. You want the server to hand out dhcp addresses.
A windows small business server does a lot of stuff, it does vpn server, email server, web server. When you configured windows server it should be a dhcp server and dns server all in a little box.
So If you turn a router on as a dhcp server, that windows server dhcp will automatically turn off. So if you put two server on the network try to handout dhcp addresses, u can cause a lot of problems.
DNS
What this does is it turns computer names into ip addresses, so if u have computer on a network looking for pc1. That computer will ask the router what the ip address of the pc1 is. The router will response with the ip address and the computer will use that ip address to contact to pc1.
Remember, computers on tcp/ip network all they care abt tcp/ip network ip addresses. The computer dont care about names. They care about ip address. The dns server response with ip address when a computer ask what this name corresponds to. The soho router doesnt have a whole lot and as much cool config as real dns server. On top of dhcp service, they hand out ip addresses , these router also acts as name server.
Port fowarding
does is: it tells router to forward specific type of traffic to specific computer on the internal network. Lets say we have a web server, it has a internal ip-address. All types of internet traffic, use different port.
Then you have a port	“ip-address:80”. Every single service on the internet uses a different port.
So in your router, in the config you say anything comes in for port:80, it should be send for some hopefully a static ip address.
So smthg comes in for port 25, you want to direct it to email server.
Small business server have 5 ports to forwards. The thing with port fowarding is all the server on ur internal network needs a static ip address. So they do not get their ip address from dhcp, you gotta hardcode.
Firewall
most soho routers have a firewall built into it. All it does, it blocks traffic on specific ports on your router so that hackers cannot try to hack into your network.

So if all your ports are open on your router, theres a chance a hacker can get into your network. Just hack your network. All firewall does is block ports. So you can block all ports and open specific ports u want open, so u have a web server, you say I want a port 80 open.
Remember, most of the time, the firewall blocks both incoming and outgoing traffic.
So if you block port80 that pc on internal network wont be able to use web service.
The firewall rules takes precedence over port fowarding.
Port triggering
automatic version of port fowarding.
Redundancy
a lot of clients go for linkses router, cuz it offers internet redundancy. You can plugin 4 different internet connection, so that any single one fail, the office will still be on the internet.
(Comcast , dsl ,verizon …)
DMZ
To use multiple routers in a normal small organization configurations.
The idea is you using one single internet connection but you want two level of internet security. So part of your network that doesnt have much security on it at all, then you want another part of your network that has a lot of security.
 So underneath of your first router, u may need this dmz maybe for web services. So u want ur client to come to ur web server that is sitting on your internet connection. Well you want everybody to get into the web server. But if that web server gets hacked, u dont want that web server to be able to attack all the client servers or other servers that u have on your network. Lets say u have a business and you want to give ur customer access to the internet. So consider u have cafee and have a WAP.
 Router 2 is the most secure. Underneath second router u may have all the other client pc.
How it works, u have ur first router, n u not gonna turn name firewall rules. What u r gonna use is port fowarding. So u gonna say anything cmg with port 80 is going to this web server.
Port 47 for vpn.
In secure network, u have email and vpn etc.
your 2nd router outbound side ip address will ve 192.168.2.3 what you’ll say to 1st router to route 25,47 to our 2nd router.

The external ip address of the 2nd router is 192.168.2.3 , the internal ip address of this router does have to be a different subnet. Router route between two different subnets. So use different for external and internal ip address for your router. So you want inside of your router ip address to be a different subnet.
Time:38
So lets say your 2nd router internal ip address is now 192.168.1.1
Your internal ip address is a different subnet.
On router 2, u gonna configure port 25 goes to the email server and port 47 goes to vpn server. Port 21 goes to active directory server.
On 2nd router u have your firewall and then u decide how secure you want it to be.
So the 1st router gonna have external static ip address and it will have some internal ip address. So traffic comes it looks for port fowarding, it’ll fowarded to whereever. If it gets to 2nd router and it then it gets fowarded to appropriate service.
Default gateway: states wheredoes the computer look if It can’t find what its looking for on the local network. So for vpn server, email server..
the default gateway will be 192.168.1.1 cuz thats the internal ip address of the 2nd router so all the computer underneath router 2 will be router 2.
and router 2 default gateway will be router 1.
Anything in the dmz, the default gateway will be router 1.
Sharing internet
Lets say u have a bldg and u wanna share internet connection between multiple businesses.
 So, u have ur internet connection up here, when it comes into the bldg you have your internet modem so whether this is a dsl modem, comcast modem, addtran etc. One of the thing most people dont realize is on a single internet connection, you can get multiple ip addresses.
External ip-address is the only thing outside world cares about. So u have 3 business, u can buy additional ip addresses.
Lets say 207.55.4.1, 207.55.4.2, 207.55.4.3
These are static external ip address.
That means the first ip address can point all of their email traffic all their web traffic etc to this external ip address. The second business can point all their traffic to the second ip address and so on.
Underneath this router, you can have a 4 port switch, not a router.
Internet>modem>switch>router*3
  On your router, u can configure all your port fowarding, firewall, anything u want.
 So one subscription to comcast business class internet, u can have multiple static ip addresses. Each business can have their own static ip address.
Router route tcp/ip.
DHCP automatically hand out ip addresses to the lan, make sure to restrict scope of the ip addresses that the router is giving out so that it doesnt give ip address that already are being used by servers or equipement on ur network.
Router have their own os sometimes called firmware or ios, so u just need to upgrade.

Powerline networking
allows u to do, is use ur electrical sys in ur bldg as ur network. So basically u plugin one of this powerline devices, u plugin a network cable to it. U plug the powerline device into a power outlet. At some other point in the bldg u plug-in another powerline device into a plug and u plug that to network cable.Now u r connected to the network.
How it works?
 U plug a network cable into this device, u plug the other end of the network cable into a switch that is connected to ur router. You connect the device to a power cable to a power outlet.

Then wherever in the bldg, u want this network to run.
 Now, u r connected to the network.

Reasons
I dont want to put a wireless card into every single computer I am using.i also dont wanna setup wireless bridge network.

Adv: sometimes small business place multiple wireless pc into a single room, the signal from all those wireless pc, starts messing everybody else. It congest wireless network. If they use powerline networking they wouldnt have wireless interference.
It uses “home plug std”.

Wireless bridges for networking

When you go out to build network for your self or for your clients, u’ll find it’s impossible to run network cable from one place to another. Lets say you r in a bldg and for some reason you cant damage the wall. So there is no way of run a cable from server room all the way to classroom on the other side of the bldg.

Lets say u r on a small facility, wer they have multiple bldgs, most of the pc are sitting on one bldg. But u may have individual workstation at this other bldg. It may be infeasible to run cable to all this individual bldgs. But u still need to get network over there somehow. Wireless bridges allow u to do this relatively simply, relatively inexpensively.
What u r doing is creating a bridge between ur main network and smaller network u creating using a wireless access point.

Wireless bridges
lets say u have main bldg with 100 workstation and u have small bldg at some distance.It’s not feasible to run network cable.
To create a wireless bridge:
In the main bldg, u put a wap connected to a switch. The wap be able to transmit network signals to the small bldg.
Now on the small bldg, u put a little wap which will be able to send and receive wireless signals between the small bldg and main bldg. In the small bldg u attach wap to a switch and run cables to their pc.
Now the main bldg and small bldg are on the network. You bridge this distance using wap.
In the main bldg, the wap connected to ur main network, instead wap u can use a router.
In the small bldg, the wap has to be a wireless access point and only wireless access point.
 In the main bldg, for your router or wap, u have to setup ur SSID.
In the small bldg, for your wap,
in config , it will ask for do u want it to be a wap or a bridge network.
Here, you want it to be a part of a bridge network.

A wap broadcast to multiple computers and recieves info from multiple pc.
A bridge access point only talks to one other access point. Once you setup the bridge, the wap gonna ask u what is the mac address of the wireless router or wap u tryna access.
So u gonna go to the main bldg wap or router and findout whats is mac address whether its on the bottom or go in the configuration.
Antenna in wap, can be replaced by powered antenna, so use good antenna. U can use directional antenna into access point and directional antenna into the router. Point at each other. Better than omni directional antenna.
If u planning to do real time communication, u wanna use 802.11.N devices.

Introduction to convergence
In old days, most electronic sys doesnt talk to each other very well. So u have telephone sys, survillance sys, acces control sys, Computer network. They didnt use talk to each other, they didnt use the same networking. Your digital survillance sys will use co-ex cable, your telephone sys use cat 3 cable. So u have all this computerized sys, they all use their own cabling and they all use their own programmin and if it does talk, it doesnt talk very well.

So microsoft, cisco and oracle , they started making system that can use same networking gear, equipment and cabling. So u have voip telephone now it uses cat 5 cabling to connect to the network. The digital survillance sys use cat 5 cabling.
All network uses same networking infrastructure.

The problem

PBX: for telephone server
DVR: survillance; digital video recorder.

Convergence allow diff sys to use tcp/ip and normal networking infrastructure.since this sys are using the same networking std, they can talk to each other.

Power over ethernet
ur network cable not only provides internet but also provide power.
U either use power injector or ur switch: which can provide power over cat5 cable to your device. Wether u dealing with a camera or Voip telephone, can get power over cat5 cable.
In power injector have a point to connect power cable and 2 ports where
 “in” goes to ur switch or router and “out” goes to ur network device.
 Power over ethernet is the greatest thing in the convergence world. So u give network device not only power but also power using cat5 cable.

Quality of Service
it allows priortize network traffic. It says voip is more imp than email traffic. It’s imp cuz the network allocate resources based on fifo.
If ur networking equipment has Qos built into it. So it prioritize voIP over telephone communication.
The cheaper equipment will automatically allocate Qos, depending on whatever is built into it. Alot of higher end equipmen such as cisco equipement u can actually go in and programme of Qos. so e.g VoIP automatically gets 10% of bandwidth.
Parallel networks
After network company come up with Qos and Convergence, they started to find out sometimes on a very large network or very data intensive application.
QoS was not good enough, the plain old Qos u still got network bog down.
Ppl come up with is use parallel network instead of Qos for different equipement on the network. So digital survillance system or computer system, so what happen each of this system get their own networking equipment
so if you go into idf, u’ll see a switch for survillance. U’ll see a switch for telephone. U’ll see a switch for computers. All though they are using cat5 cable, what they have done they have redivided this devices onto their own network; onto their own lans. So this individual lans connected down to the mdf, again they would have their own core switches and router down there, and they dont necessarily talk to each other directly. What they have done is they have router between this core switches so any communication needs to be happen, they happen through this core routers.
The main reason for this is, sometime if somebody misconfigured a survillance camera, it will push through so much data, that it will bog down the overall network.
So on larger netwrok instead of having Qos they run parallel networks.
In switch classes, they wont actual 3 individual switches in the idf, what u can do is u can have one switch seperated into multiple vlans. So one vlan would be for survillance sys, one vlan would be for telephone system. One vlan would be for computer sys.
Intelligence at the edge.
Engineers coming up with, to eleviate some of this bandwidth problem is to push or pushing the intelligence to the edge of the network. So bascially all of the intelligence is sitting on one main server. So u have a lot of dumb terminals that communicate with that server.
So on the converge world, they trying to make devices on the edge of the network so either ur telephone or ur digital camera. They trying to give that more intelligence so it doesnt have to use so much bandwidth.
So on enterprise, we are talking about 100 of Mpixel camera that are all pushing data at the same exact time. Thats a lot of switches, router. A lot of network infrastructure, when most of the time, those camera gonna be looking at an empty parking lot. So engineers are doing is trying to build intelligence to that device, so in the main server. They can actually programme and they can say when they want this camera to transmit info.
This ip devices: telephone,camera,access control sys is having intelligence so they can act without having to talk to the server. Thats a lot of data to be push through switches and more expensive the switch u have to buy, etc…
The cheaper the better.
With convergence, you can actually launch a call straight from outlook contact.
In cloud computing, we are putting intelligence to one main server.
In converged world, they are trying put intelligence to device. The more decisions that device can make, the less data has to transferred over the network.

 Network mapping

You plugin into a network and u try to figure out what is on the network. What services are available on the network. What shares are on the network. What computers are on the network. What accesspoint,router,server etc.
Big problem especially for consultants coming into a computer network, thats already up and running. Many times u have absolutely no idea what is on the network. The people they are hiring you, they really have no idea whats on the network.
Being able to map the network, u can figure out what is on the network. So bascially u can figure out where to go from where u are.
Alot of modern networking equipement when you plugin it into a network, it uses a dhcp to automatically grab a ip address. So u plugin a wap, network printer etc. if u know the ip address, u can go to ur pc and u go into a nice little interface and administer the printer, wap, router.
The problem is u dont know what ip address that device has the problem Is It very difficult to get to it. By understanding network mapping, u can automatically map an entire network, be able to find all ur pc,wap,router,printer….
How to map a network.
Basic services u use to map a network: ICMP, port scanning, smb(server messaging block,snmp …. tells the basic process of doing just so u have a overall idea why u map a network.
This can be use as a consultant going in, to figure out whats going on the network. What the servers are, what the access points are ….
This could be use for security, to find out what shares are open, what shouldnt be open. What ports are open.

When u doing network mapping, there is 4 basic components to the sys or to the networks for u to understand.
ICMP(Internet Control Msg protocol), this is a protocol that is part of the tcp/ip networking suite.
Within that tcp/ip there is ICMP, this is the protocol that allow computers and networking devices to talk back and forth and send error msg. So on the very lowest level this is how computers and devices can talk and make sure there another device is there and if its not there can send error messages back.

Basically, we gonna use icmp for is smthg called the echo request. Echo request is where your computer calls out to a computer or device on a network and say hey are u there to some device. The device is supposed to respond back say ‘yes I am here’. With echo request 3 things happen your computer tries to talk to that network or computer device and that device comes back and gives u an echo response that is crystal clear. Or you can get an echo response with info , within that echo response you can see there are errors. So its not that the network cable is unplugged entirely or that the network device is powered off but for some reason the communication isnt going back and forth as smooth as possible.
You get 3 responses: Good, some problem, no response.

Port scanning: all networking services uses ports within the tcp/ip protocols. So if you are going to a web site you use port 80, ssh if you’re using to get to a linux server you’re using port 22, if you are using pop3 email access you’re using port 110 so every single network application uses its own port. So what we are gonna be doing is port scanning to see what computers have what ports open. By seeing what ports are open we can can determine what the computer or server might be doing. So if its ftp , that might be a file server or somebody accidentally turn on ftp and we should turn that off.

SMB shares servers message block.
Generally used with windows networks this is where you dbl click on shared folder and u can access shared folders, shared files , shared printers on other computers. These are smb shares
SNMP:
to send greater quantity of info to network administrator so they can fully understand what is going on with their systems and their servers.
U have 3 things (1) U have network management system goes and it gathers info from all the computers and devices on ur network that are using snmp. Those computer and devices on the network that are gatherig info then have snmp agents installed on them so this are small little piece of programming and then what you can do is you can create snmp traps that state when something happen with that device or that computer, u wanna send alert back to network management sys.
How snmp works in real world, is basically lets say u have a server and u worried that u dont want this server to go over 90% cpu utilization so what

u can do is install snmp agent onto that server, then u can create a trap
that say if the cpu goes over 90% usage for 5 min, I want the network management system to be alerted. Using snmp agents and traps, u can gather all the software that is installed on your that computer, you can determine what update are installed on the computer. You can determine all the hardware is on the computer. So imagine u have 100 of computers in ur network, u can sit on your console and see what computers have only 2 gigs of ram, all hardware info from network management system, etc.
Remember about snmp is that there is a simple network management protocol service on ur windows system( that has to be running), if u turn that off, snmp doesnt work at all. It also requires UDP so not TCP, UDP port 161 and 162.

DOS Tools
 ipconfig: ip address info of your computer.
ipconfig/all: subnet mask, ip address of ur dhcp server , ip address of default gateway, ip address of your dns server.
The default gateway is ur router, ur cable modem, ur adtran, whatever gets you from inside your bldg out to the internet cloud.
Dns server:
if u have a very simple network, then ur dns server, your dhcp server and your default gateway will all be the same device. Whether its a router, windows server. Dns,dhcp, default gateway will all be on the same device.
If u r on a complicated network all those will be on different device.

Ipconfig /release: this will release the ip address that ur pc currently has.
ipconfig /renew: this renew ur ip address and make sure u have the most current ip address info.

To make sure you can talk to other pc on the network.
The first thing that we use with this icmp communication protocol is the command ping.
Ping does: ur pc call out another device on the network and ask it its there.
Ping [ip address/domain_name]
so if u r trying to find out, u r communicating wid ur default gateway I.e wid ur modem. This will tell me if I am talking to my router to my default gateway. If it says error cant be found then I know I have a major problem inside ur network. After u do ping command, it will call out and get a

response 4 times. If u r in linux world, it will continiously ping until u force it to stop.
When this does this 4 times, basically it’ll go out it’ll ping the device and then it will you the time to live, it will tell u how quickly this communication happens, if u have a high no that means u have a delay in the system. If u have low number, uk everything is doing pretty good.
Now when u do a ping for domain name, let say a server. It will ping as long as your computer can communicate with a dns server, the ping command will resolve the ip address of the server that you are trying to get to. Lets say u are trying to get to the exchange server, so u do ping exchange well then the ping cmd talks to the dns server and it will then figure out what this ip address is, and then it will ping the ip address. U can see whether ur exchange server is up and running and it then also give u the ip address of the exchange server.
Ping /? :- to get help
lets say it pings 4 times: 1,2 is good, 3 is a bit bad, 4 is good.
So u wanna determine how flaky that the network connection maybe. So instead of sending out 4 pings, you wanna send out 200 pings.
Ping ipadress -n 200
Sometimes the server is very slow to respong to your ping request, so u wanna use ttl; it says if I didnt get ping response in some ms I am going to assume the ping cmd failed.
Ping ip address -i 200ms.

The next thing u wanna do is try to isolate where the problem is in the network. Trying to understand what routers or networking equipment are routing your traffic you can use trace route cmd.
Its like a ping cmd, the diff is it gives u an echo response from every networking device that you go through.
Traceroute <ip address> or tracert
u’ll see all the hops basically all the router it goes through to get to server u trying to reach. It goes though so many gateway.

Ping works for pc, router, printer, wap, depending on what u dealing it may also work for ur switches. It works for diff networking devices that is using tcp ip.

Ipconfig /release it will release the dhcp ip address that we currently have on the system.
Ipconfig /renew
ipconfig /all
time:25

Host name: computer name
Ethernet adapter local area conn > description
: name of the adapter
physical address
ipv4 address
default gatway is the networking device that gets us out to the world. Whether its a router, dsl modem,etc.

Networking mapping software:

what it does is, it tries to go out and grabs info about ur network. Now, the network mapping software some of it is free, some of it is open source.
That this software n all the different version of it, are build to do different things and do differently, some of it will give u simple text file and some will give u fancy pictures and show u how all the devices connect to each other.
Some all they do, is look for open ports and open shares.
Others map everything and it will tell u all the software that’s installed in each and every pc.

Software:Port Scan
scans all devices in the network, n looks for open ports and smb shares.
Spiceworks: it can inventory software on computers, it can determine what types of devices search and networking equipment are. Also, It will tell the os on network device

Security
the more things the more services u shutdown, more complicated it’s gonna be to administrate a network. So u can close down all these services, u can turn snmp, u can turn off ping request. But if u do that it will be very difficul to amp that network if another technician comes behind you or something just weird happens. So if u wanna shutdown ping service, ping is the basic service that all of these network mapping use o determin if pc exist. So u can shut down icmp echo request. So if u have router sitting on the internet, u dont want any1 to ping that router. So in router settings, we can turn off ping request, so it wont response to that request.

If u want the pc on ur network to stop responding to icmp echo request, u have to install security software(Mcafee, avast).
In your windows u can turn snmp service off.
Or you can use a firewall, it uses UDP port 161 and 162. so if u turn off the firewall for that local computer and prohibit outbound traffic on port 161 and 162 that would stop the snmp from working also. Those are the way to secure your network. But think about it a lot snmp is a very useful tool

 -using scan u can find old and obsolete pc.
-snmp agent and traps u can make sure all ur computers are upto whatever hardware and software standards that you require. What pc have a slow processor.

TCP/IP and subnet masking

Transmission control protocol, internet protocol
tcp/ip overview:
is actual a protocol suite that is made up of tcp and ip protocol, with few more protocols too.

IP: is a protocol within tcp ip that controls routing info to different computers and different servers on the network.
IP protocol deals with things called ip addresses, subnet mask, default gateway, dns etc.
Ip protocol let 2 computers to figure out where the other one is. So they can start communication.
IP is a routable protocol. So , tcp/ip is a routable protocol.
There were in old days, routable protocols and not routable protocols.
Which means;
Routable protocols; what this meant u can divide networks into subnetworks.
In non routable protocols: every single computers can talk to each other
So u plugin into a network a non routable protocol, all those pc are connected. This cause absolute havoc. With bandwidth utilization with all this different pc try to talk to each other. Imagine if every single pc on the internet are connected to every single compuer on the internet at any one time, it would be havoc.

What ipx, tcp did is: that we can divide all this network into multiple subnetwork and then u have a boundary which was ur router and through the router this computer can try to connect to other networks if need be. Anything on the subnetwork can talk to each other.
But if a computer in one subnetwork wants to talk to computer on another subnetwork. It will go through a router, it will go through the internet and such and go to the subnetwork.
Routable protocols allows u to divide huge network into smaller sub networks. Being a routable protocols you connect sub-networks using router.
OSI model is a model for how netwrok communication happen, ip is on OSI layer 3, the network 3. IP is about routing info, is how computers discover each other. So they can start communicating. Once the computers have found eachother, they do need to start communicating, thats where tcp comes in. This deals with once computer have found each other. How are they going to talk. What language are they gonna talk, how fast they gonna talk, etc.
In tcp, something called windowing, is the process by which the client computer sends info to the server computer. When two computers are tryna talk windowing is the process how the data is sent from one computer to the other computer.
In windowing, lets say pc1 wants to send data to pc2.
In tcp/ip we want the data to be broken down in something called packets,
those packets are send to a computer that is receiving the data, since the computer dont know what the quality of transmission line are, the first document doesnt want to send all the info all at once, cuz It may come out as garbage to the other side. So what it does it starts sending packets in groups and groups gets progresively bigger. What happens in windowing process pc1 sends one packet all the way to pc2. This packet may be label as packet1. The computer 2 will receive packet1 and it will send acknowledgement to packet1. Now that pc1 understand it can talk to pc2. It tries to send a little more info. So now it will send packet2 and packet3 over to pc2. The pc2 acknowledge and says last packets I received in order is packet3. So pc1 thinks this a nice conn, so It sends packet 4,5,6,7 over to pc2. The pc2 receives packets and acknowledge that I got all info and the last packet I receive was 7. As long as the communication is solid, the pc2 sends twice as much info. As long as pc1 recieves acknowledgement and its in order, it keeps doubling and sending larger and larger chunks of info.
But If smthg happen on the way and the data got messed up what may happen pc2 only receives 2/128 packets in order. The pc2 will say hey the last packet I received in order is 1034, the pc1 what will now do, is it will start sending info again and it will close the window back to single packet.
This keeps happening until theres an problem with the data communication and it goes back to sending one packet.
When u were downloading data from website, ull see a progress bar. It will stutter. Small increments and huge increments, small increments and huge increments.
Tcp ip4 can be real mess for real communication.
Ip connects two computer together, tcp deal with info once they start talking to each other. Windowing is how is data is transfer from first computer to second computer.
TCP is OSI Layer 4. Transport layer

How tcp/ip works
ip address: every device on the network needs an ip address.
subnet mask is a way to segment a network logically so that different computers and different device cant necessarily talk to different devices on the same physical network. So if u have 200 pc on a network, u dont necessarily want all the computer on the network to talk to each other, even though they are physical connected to the same network. You can prevent them from talking 2 each other by putting a subnet mask.
Default gateway is the router for the subnet network thay you are on,
so basically what the default gateway allows is ur computer is going to look on the local network for the computer or device that it’s looking for, if it cant find in the local network it will then go to the default gateway. It will ask the default gateway to find that computer or device on whatever else is on the other side.

INTERNET

ROUTER
PC

So ur computer with it’s ip address is looking for website, so basically what it first do, it will look for a computer in the internal network. If it’s not there it will use this default gateway, it will then go to the router and that router will go out to the internet.
Ip connects computer using ip address.
DNS server do: map domain name to ip address.
So what domain server do, is it map domain name to <ip address>
To find some website, ur pc talks to dns server.
Then when ur website knows the ip address it then looks in the internal network for that ip address, if it can’t find that ip it goes to ur default gateway and ur default gateway goes out to the internet and it then connect s u to the site.

DHCP: every device on the network needs an ip address. Not only it cant receive communication it can’t talk to anybody. Every computer in the network needs to know its ip address, default gateway,subnet mask, dns server.

There are two ways of giving computer this info: (1) static ip address : what this means u sit down at ur computer or device and u plugin info manually.
Also if u give 2 pc the same ip: some packets go to pc1 and some packets go to pc2. Havoc!
Dynamic ip addresses: when a computer connects to the network, it will call out the dhcp server, the dhcp server will give it a ip address.it will tell the subnet mask, default gateway, dns server automatically and keep a record of it.
Lease: u have lease time in dhcp given ip address.
What happens half way through the lease, ur computer tries to automatically renew the ip address. Ur computer will say to dhcp that I am still here, I would like to keep using the ip address do u mind?
It goes on and on.
What happens if ur computer can’t contact to dhcp server on the 50% mark, then it waits until next 50% mark.
If for some reason the dhcp server is offline, then ur computer again ask on the remaining 50%. if u still didnt hear back from dhcp server, u wait again for 50% of remaining time. And it goes on and on.
All the way to the end, it depends on the networking software u have installed on the computer, It wil flush out the ip address and other time it will keep it.
The shorter ur dhcp lease, the more network traffic u have, but that means less ip address are being used by pc that may not be on the network.
The longer the ip address, more ip address get used up, but less traffic on the network.

NAT (Network address translation) :
back in the days ppl were worried that they thought every single device
on the internet will require their own dedicated ip address. That means ur computer will require an ip address that will be unique to the world not unique to ur office. You’ll see most internal networks have ip address ranges from 192.168.1.1 to 254
So u go into ur little network inside ur house, ur computer in the house may have an ip address and u go to ur friends house his computer also have the same ip address.

How this happens, is using network address translation what happens that every router that connects to the internet( whether this is home router,business router , enterprise router). Every single router connected to the internet needs its own dedicated ip address.

When u r trying to communicate to servers on the internet, the server is gonna be most worried whats ur external ip address is.

So NAT allows ur pc goes to ur default gateway and its gonna out and find ur chosen website, the website gonna say the communication came from this particular to router, so it will send the info to this router( this router has nat build into it) and it say ik the internal ip address and the info get route to ur pc.
Default gateway are routers what connects different sub-networks.
Whether u have multiple sub-networks in one bldg, or u r trying to connect ur office network to the internet. Default gateway or router is what seperates those two networks.

Subnet masking
You need to understand where we come with this no’s, when we say 10.1.10.1 or 255.255.255.0
 Basically they are number values for octet, when u dealing with tcp/ip addresses u dealing with 4 Octets. Octet are series of 8 numbers.

10.1.10.1
- - - - - - - - . - - - - - - - - . - - - - - - - - . - - - - - - - - <!-- 4 Octet

128 64 32 16 8 4 21
- - - - - - - -

Subnet masking
192.168.1.1: tells u the address of the networking device on the network. There’s also the subnet no or the network no.
 so the ip address tells u an identifier for the network and tells u the identifier for the networking device.

So u might be wondering what part of this,is for the network, what part of part of this,is for the subnetwork. That’s what subnet mask tells u, so u got
255.255.255.0
It tells u what part of this is the netwrok identifier and what part of this is device identifier. This is very imp cuz devices on different networks can’t talk to each other. So if u have one computer plugged into a switch on network 1 and u have a printer plugged into the exact same switch, so they physically on the same switch.
The computer that is on the first subnet can’t talk to printer if its on a other subnet or other network based upon ip address unless there’s a router to connect them. Router connects different subnets. So if u have a router in one network and a printer on a diffferent network, they need a router to communicate, even if they are plugged in physically to the same switch. So u can have multiple subnet all plugged in to the same physical switch. This isn’t like cisco vlan; this isnt routing and switching vlan.
This is simply how tcp/ip works.

So if u have computers on different subnets, on different networks, even though they are connected to a switch physically they cant talk to each other. So this subnet mask is what tells you what part of the ip address are for the network and what part of the ip address is for device on the network.
So 255.255.255.0 is what called a Class C subnet.
Since ik whats going on, I can automatically look in this class C subnet and know the network portion of this address is 192.168.1.X network, so I know the identifier for the device on the network is 1.
Using this octet, we decide how many networks we need in a network and how many host we need in our overall network and then all we do we use that many bits that we need to accomplish are task. So we divide it off in anywhere in here.-----|--------------------------
so we want anything to the left to be the network number and anything to the other side to be the device no. we can decide wherever I want to put the line between.we can decide depending upon subnet mask.
It depends upon how many networks u trying to create or how many netwo rk u trying to shove into a single network.

Depending upon how many bits u use on the network, theres an equation and for the network is 2^n
n is howmany no of bits u used for ur subnet.

So if u wanna use first 8 bits out of the 4 octets so 2^8 it will tell u how many subnets can u have for ur network.
If u r trying to find host so
 ------network|host-----------
 u have -2 + 2^(n)

so u have 255 host and that is using 8 bits from the first octet so its class C subnet.
I.e -2+2^(8) =254 host
so what u r doing when u creating a subnet, u have to figure out either how many networks u want or how many host u want and then depending u basically count one way or the other-----------------|---------
so If u need lots of network, then u count out how many bits u need from left to right and then u take those bits for ur subnet network.
If u need to figure out how many host u need, u go right to left and u take the bits as u need.
So if u r dealing with this, all u do then to figure out the subnet mask is.
4 octets.
 So u add up all the bits and the number.
 A class subnet is 255.0.0.0
 B class subnet is 255.255.0.0
 C class subnet is 255.255.255.0

Since you are really cool engineer, u not gonna divide the subnet based on the octet. Sometimes you got to be crafty,clever and use not 255 subnet.
Your network administrator gives u class 3 subnet
so u wanna divide this into two networks.

 128+64=192;
 So we can now use this two bits to create different networks.

So if u have 255.255.255.192
that mean we can use this bits to create different networks.
The main thing to understand is when u doing subnet mask, whatever bits u used are used for the network, the subnet identifier, other bits are used for computer identifier.
 They cant talk to each other based upon tcp/ip protocol , u have to put something called a router in between to get this computer to talk to each other, even though they are connected to a physical switch.

we can draw a line to seperate our host bit from subnetting bits

 so /24 is known as cidr notation
classless inter domain routing.

This will tell how many binary digits are turned on a subnet mask.

This all are subnetting bits and everything else are considered host bits.
21 bits are in our subnet mask.
e.g

 we are given the mask and we are given /21 from that we can figure out what the actual network id is
so we can say 192.168 is part of the network id cuz the mask includes all 1’s there. If all 1’s it means use this no, the mask means use the numbers wherever the mask has a 1.
so if first two octet in our mask has 255.255. then we know we need to use first two octet of our ip address in our network id.

The subnet mask tells us what our network id is.
Subnet mask, network mast, subnet id, network id.
Above tell us that 40 is also a part of our network id, cuz the bits that goes along with the extension of our subnet mask includes 40.

if above if we have 192.168.41.55 then 41 wouldnt actually be a part of our network id, cuz our mask says only use this bits where’s a 1 in the mask.
E.g
Above we have entire 4th octet and 3bits from 3 octet are all host bits.
 128 64 32 16 8 4 2 1
Our network id 192.168.40.0
E.g

if I add all this no, 32+16+8+4+2+1
 it will give a broadcast for the network, which in this case .63 and that is always 1 left then the no left to it. I.e 64-1.
the broadcast for this network is 192.168.45.63, if something is sent on that address, it will be sent to everybody on the network. It also tell us how many host ip address or how many usable ip address if we add all this up to 63-1(broadcast), then we have total of 62 available addresses in this network. 62 host. We have to assign one to our router so 61.

Terms:
subnet mask divide computer into different subnets on the same physical network.
Default gateway: are router that connects ur subnet to other subnet.
Cidr: classless inter domain routing.
Server:
server: windows 2008,2003 server, ubuntu server, red hat linux enterprise server edition.
A server which has a server in his name: windows 2008 server.
A server doesnt have to have word server in the os.
Server: all a server is that provide services to other computers on the network.
File server: is a computer on the network that have files into it that other people can get to.
Print server: is a computer with a printer attach that can share out that printer to other computer on the network.
Web server: is a computer with some special software installed on it that allows that computer to present websites to people going to that computer.

Image a real server, a active directory server, that means people logged into it ang they gain resources to the network. A real server are much more robust and can support a lot of incoming request.
So the server can support upto 10k users so that server software is much more robust and can deal with far more users and issues than a little desktop os.
Real servers are much more complicated than desktop computers because they dont come with many of the nice litte friendly users tools than desktop computers with.
Whenever u installed a piece of software to the os, not only do u get the extra functionality but you also get possible extra flwas bugs and defects that hackers can use to compromise the system.
So u installed flash in ur pc, so u can watch videos in ur pc, but the flash has security holes that hackers can use to take over the computers.
So vendors when create a os they dont put as many of those nice little features into the server os.
So its a lot difficult to administer window server than to a normal windows computer.
So dos prompt is most secure.
In Server os:
 When u go to buy backup software or utility software: thats gonna be expensive than normal comparable desktop version.
Even a disk partioning software for desktop is kk
for server is insane.

Server hardware:
use real server hardware if u want a real good uptime.
Server processor: intel processor:xeon server: cuz this processor is build for dealing with the task that servers normally deal with.
Redundant power supplies
raid-3 (redundant array of inexpensive disks)
allows you to combine multiple physical disk into one logical disk.
Disk striking with parity or disk mirroring
disk mirroring: is when u have two hard-drives in a machine that are identical. These are hard-drives are hot swappable, so if one hard-drive fails u pulled out the drive that failed and u plugin a brand new hard-drive, the computer does something it calls it rebuilds the array and then you go back to being redundant.
Raid-5 is where u can combine 3-32 disk into one logical hard drive, what it does it stripes the data that u have acroos all the hard drive that u have in the raid and u have one hard-drive that is used for parity.
So basically if u have 5 hard-drive, basically it stripes the data along those hard-drive and use one of the hard-drive as a recovery drive. So if any hard-drive fails, u pull that that bad hard-drive out, the computer still seems functional you put the new hard-drive in and does something called rebuilding the array, so ur server never shutsdown.
ECC ram: incredibly expensive, when u start ur pc it does a self test to that ram to make sure that ram is functioing properly and if not it does a couple of corrections. U dont have to worry about having a bad ram.
If u have a web server, or something that is crunching a lot of info. It cause problem, like a little snowball get bigger as it falls down the snow hill. Ecc ram make sure ur ram is perfect and if its not it makes corrections.
Types of server:file,ftp,web,database,ternimal services, etc.
A server can do multiple things; a mail server can be a ftp server and an active directory server all at one time.
  When you buy windows 2008 server, most of the functionality is already build into it, so piece of software are already included in the os that u get.
So when u get windows 2008 server, not only u get a server os, the file server,web servers,iis(internet and information server), ftp server,terminal services server,active directory server is already built-in. If u r using linux, u have to install all this pieces of server software individually.
So u have to install and setup.

You can buy software on a noraml desktop computer so it can have server functionality. So If u want a fully functional web server on a window xp home computer, u can download for free, something called apache web server and this makes that little window xp desktop computer a full web server or you can isntall mysql database it can be a database server. There is fileZilla server so it becames a full fledged ftp file server.

Authentication
u have to login into the network. There is a server on the network that allows access to the network. This is called a authentication server, so in windows world, they use something called active directory server, bascially u sit down to log in to the network, so u pass credentials to active directiory server, the active directory server gives u a access control key digitally. This access control key say what permissions u have to do things on the network. In windows it’s called active directory and its provide by domain controllers. If u using linux they have a samba server, not as good as windows active directory sever.
Print: printer have built in print server.
File:
web:2 piece of software for websites: apache, in windows world u have iis internet and information server, theres a version built into all windows os, if u deal with windows server 2008 operating system, u have full fledged version of iis and u can present world class website using that.
Ftp: allows u to transfer files from one place to the other, so if u r trying to upload files onto your website you would use ftp, this is different than a normal file server. A file server uses a special protocol in order to transfer files back and forth. Ftp uses a different protocol to transfer files back n forth. Ftp severs normally sit on the internet and allow u to upload large files to them. They are normally included with web servers.
Email server:
software specially designed to route email, all the email for your company goes to one single server, and that server will decide what to do with it, wherever it needs to go.
Micrsosoft exchange server and whenever anybody logs in using outlook, they are able to get all their email off of that server. To have microsoft exchange u need to have windows server, it only runs on windows server.
Database server: all outside app to put data into it and pull data out to manipulate the data thats there, all they worried about data, they dont have fancy interfaces, u have to put sql commands.

Database software which isnt free is microsoft sequel tha runs only on microsoft sequel server.
Remote access: nowdays these are normally vpn servers, it allows u to connect to the server and from there have access to rest of the network.
So u r on the internet and u have vpn and u have remote access server, so its this remote access server you can connect through the internet to that server and once you connected to that server you get the resources that are in that local network. Shinchan fax.

Trouble shooting methodology
everybody runs out and get ms certification and cisco certification. Not every1 goes for trouble shooting methodology and not how to actually grasp how to find the problem u need to fix.

Everybody learns to fix a window server, nobody learns its the window server.
If u know whats the problem then u know what to learn, what to target.
Idk what that is, idk what that really does, but ik that thing is broken.

Introduction to troubleshooting methodology

warning: to be very careful ,its very easy to create one minor problem and create a massive major problem. Go slow, anytime u taking a server off of the network from the server room, when I go to unplug the cable from the switch, I’ll trace the cable from the server all the way to the switch to make sure I know I am pulling the right cable. Cuz I am thinking the cable from the web server but I actually pulled the cable from the active directory server. It’s better to be right than be fast.
Realize that u r going to breakthings during the troubleshooting process, part of fixing somethings is u have to break something else to make it work, u have to other things offline, u may have to replace parts, u have to deal with sys or technology that are out of ur speciality. It’s like chess, u go slow and u think 2,3 steps ahead.so I think this is the problem so who can I call or who do I get authorization from to work on this. If you keep going that way, if u r working on something and u realize that u may break it, trying to fix it, if it does break then keep it in the back of the mind, even when its still working, if it breaks, how do I get this fixed.

If u r slow and careful and u always thinking 3,5 steps ahead, u r gonna be okey.
Size up the situation:
1st part of the troubleshooting process is sizing up the situation and communicating with everybody that needs to be communicating with. So u get called that theres a problem, so u talk to the person telling u what the problem is, is either a employee says that my computer cant get on the network, or is the manager saying all my people computers cant get on the network, go to the person who is complaining, go talk to them and figure out what theirs complain are, once u have done this, go and talk to anybody else that maybe affected by the problem. So if its manager is saying his division or anybody in his little area cant get on the internet. After go out to few employees and talk to them what they think of the situation. So is the problem is going on for a while, did this happen today, so u wanna get as many viewpoint as many as possible, remember ppl dont mean to lie but a lot of time they present u with incorrect info. So if u get info from one source,then u may be getting incorrect info in the working off of it. If ur talking to a manager and if ur done go talk to few of the employee, make sure u understand what the problem is and the manager actally understand what the problem is, during this process u also need to find out who is ur point of contact is, who is the person who actually makes decision for what u going to be doing. Lets say ppl on the office cant get on the internet, u may need to take down the switch or u may need to takedown a networking component to repair the internet problem. You need to find who you can ask when you can take everybody off the network so u dont want to go in and unplug something and nobody can get to any shared files anymore, cuz if u do that u create a larger problem.
During the process u trying to refine down and figure out what’s exactly going on and also see if theres a larger problem, sometimes during the conversation processes you find out theres a bigger problem says that manager says that nobody can get on the internet. You talk to the employee and you find out not only they cant get on the internet but they also cant get to any shared files. So its a bigger problem then what u realize. You find this out by communicating to people. You also need to find out who and what is affected, what sys are affected by not this being able to happen. Also talk to people why is this important does this mean, ppl cant get to yahoo when they are bored during the day, thats not a high priority.
You not gonna take this as seriously as if this the payroll department and they have to get on the internet because payroll is due tommrow.

Or payroll is due, but payroll is due in 3 days, so u figure out this needs to be done in 3 days, this doesnt have to be done in 1 day. This types of question and figure this type of stuff will help you prioritize the problem and as u go forward with troubleshooting process determine what steps u take, lets say payroll has to go out tommorow, u’ll do different things that if payroll has to go out in 4 days. If payroll is due in 4 days you may trouble shoot the problem down to the router well its 4 days, routers are expensive so I might try troubleshooting that router and see I can fix the router it’ll be less expensive than buying a new one and everybody is happy. It takes longer and its still under the timeframe that you have, well if its 12 hours or 24 hours so that payroll goes out screw it, I am buying a new router, I am throwing a brand new router and then payroll will go out tommorow. Ppl arent happy, but payroll went out which is more important than the cost of the router.

So talking to people and figuring out ur time frames, this will show u the problem is larger or smaller than u first realized. What time constraints u are on, and when u do figure out the problem how u gonna deal with it. So u gonna spend 3 days troubleshooting it or you just gonna get a new1. Once u figure out all this info and u gonna back to the point of contact and to the person who first logs the problem. You are going to tell them, what u think is going on so u know they give u the problem and u say its a networking issue and this is how I am going to proceed from here and give them a brief idea what you’re thinking and tell them and whats going to happen from this point. When u do this do not lie, one of the most important things in communication and technology is under promise over deliver . Like I think this gonna take 4 hours and u proabably need a new router and how much gonna it cost.

Research and planning
u have an idea, the next step is who to call and to figure out what to do, if its a web server problem see if there is a maintainance contract on that web server whether its maintainance contract on the hardware problem or is the software vendor solution, where somebody is responsible for maintainig that software.while ur troubleshooting u should continiously researching and continiously understand whats going on.
If it turns out to be the web server by the time you troubleshoot down there

then u already know what to do next. As u r trying to figure out all these other things, u say I see there’s the web server on the network is there a maintainance contract with that, yes, so u go tell the point of contact, u can tell I troubleshoot it down to web server, I am not authorized to touch it, it’s under maintainance contract.

Troubleshooting takes time, talking to ppl , tracking down paperwork, getting ppl to call u back takes time. As soon as I figure out and I have an idea whats the problem is, I have an idea what the solution is. Like right then and ther, like I say with the web server if I think the problem is the web server. To the point of contact I can say it may be this web server kk, is there an maintainance contract on it, yes, do u know what the terms of it are, NO, do u have another point of contact for the web server, yes I do, heres this person phone number.
As soon as you get that phone no, u call the person and say I understand you are the point of contact with this web server, I am with this company I am trying to fix the network problem, idk if its a web server yet but if it is what do I need to do to get you out here.
This process is going while u doing other troubleshooting process. U do this with web server, u do this with the network, other server and isp. Whatever u may think thats part of the problem. You walk into a company where their networking systems are contracted out to another company and maybe their server hardware is contracted out to another company. If u called all three of those companies while you’re doing the troubleshootig process, then when u narrow it down Oooh its a router. The networking people already have a heads up and so when you call them back you can look at the whole process you done quickly. So with this research you try to figure out who’s responsible for what is it internal like if you’re an employee its a department or division other than you or it maybe a maintainance contract so it might be something outside of your company entirely and if it isnt maintainance contract then who is the internal person to call for that maintainance contract because all we know u have an account number manytimes they dont let any avg tech call via or IBM or oracle they dont want anyboy just calling them up because it cost of 500$
an hour, so if u have an maintainance contract u need to figure out who is the one making call for it and then figure out how all the system kind of work together so you know you’ve got this web server, talk to ppl and figure out that connects to what network who is responsible for the

network, what is on that network, how many web servers do u have in this process, do research and figure out whats going on like I say research is an ongoing process during troubleshooting so the better u get at researching
and talking to people as you’re doing the troubleshooting process the quicker u’ll end up being able to get the problem resolved. Because like I said if u wait all the way till you figured out exactly what the problem is before you call anybody else then you’re going to wait another two hours for them to call u back, whereas If u give them a heads up two hours ago, u figure out what the problem is, it gets fixed quicker.
Points of failure:
eagle eye view whats going on.
When u doing troubleshooting and u find out the device thats causing the problem, that u may not had any busines fixing, so u narrow it down and say its that black bix right there.
A company have a web server: a website that ppl goes in to put in their payroll, so u have main headquaters office somewhere and then a remote office gets on the internet and accesses the web server.
For some reason ppl at the remote office cant access that server, so we need to figure out whats going on?
So first thing we know this ppl need to go throught the internet to the home office. You may have a problem with dns, security certificate,etc.
In general internet problem.
The remote office uses the internal network to connect to the internet, the headquaters uses a internal network to get to the internet too.

It could be the internet, remote site internal network,headquarter sides internal network.
Then we get pass that then we have the actual workstation

so the computer that goes through the internal network to get to the internet to go to the other internal network that could be the problem. Maybe it has a virus, maybe IE is buggy or on the other side the server that host the website

so we know there are 5 large area that maybe the problem,
1. it could be the desktop computer or computers (client)
2. it could be the internal network
3. it could be the internet( dns, ip address is pointed at wrong place)
4. it could be the headquarter office internal network problem
5.web server itself.

Now I troubleshoot all of the components, now who do I hand off this problem to, this how u divide the problem into eagle eye of view and find out the major points of failure or the problem could be.

Break problem into pieces:
now u have the eagle eye view of how the system works, then u start going in and trying to say either large chunks of the systems are good or they might be suspect. Once u narrow down to particular computer or server u can be very specific on the troubleshooting technique

 when this computer cant go to this web server here, there could be a lot of issues going on, u dont wanna be doing very very

specific and precise troubleshooting at this point, because its gonna be a waste of time. What u wanna do is eliminate large chunks of this whole system and to say its probably good. What eli does, he tries to work from the outside and work in. As I do that I try to eliminate as much as possible.
Kk so he goes to desktop and say u cant go to the website at the headquarter office, can u get any website at all.
By seeing that we know that their internal network and part of the internet is working. So its probably good.
Then we go to the web server and say is the web server working, I will on the server itself, go to the browser and see can I get to the website. So u open the browser and it goes to the website that has localhost.
If its say 404 not found, then the server isnt giving a website to anybody.
So the web server is definitely the problem.
But if its 200 status code, the web server is kk

so u now go, somebody thats in headquarters bldg and say can u do me a favour and pull up this website internally.

Inside the headquarters bldg somebody at a computer then tries to go to the website, they get to the website just fine 200.
that means thats not the web server in ur internal network.

So the web server is good,
the headquarter internal network is good,
the remote site internal network is good.
So the question is left, is it the computer on the remote site or is it the internet, maybe theres a configuration problem in the internet.
Well, depending upon how many remote offices u have, hopefully u have a couple what you could ask is if theres an another remote office can they on their computers get to the website. So u can call up another remote office you say hey can you just do me a favour can u try to get to the bldg website right now. They go in and they get to the website, so the internet is fine. So the last thing u left with is the local computer. So u can then ask to other people on the office r u having any problem, NO I AM Not, so other people on the computers are working kk, so it must be this specific computer here

You find out some securtiy setting in the browser is messed up.

Troubleshooting the device

most problems comes out because things have changed, so whoever ur point of contact is, or whoever is responsible for this computer whether its the secretary or whether its a other technician whether its an outside firm, u need to find out something happened to this device between when it was working and when it was not working. U can think about unintended things say power outage and thats when internet started acting a little weird, so u have spike of electric shooting that network, maybe the router got fried, so may be a hardware issue with this.
2) has anything happened that is intended, did somebody do smthg.
So lets say 1 person tries to get to the website and u ask them this was wrking on monday right, today is wednesday its not working YEAH
did u do anything on monday or tuesday.” I was worried about my security and I put on a norton security suite. OoOo
So u can narrow down.
Maybe it was an os update, if u dealing with cisco or networking equipment and there was an iOS update, maybe they update the latest iOS and it was faulty, they updated it and they didnt realize there it is. Then u can say this, most likely the problem is this so we need to fix it. We understand what to do, is uninstall norton internet security suite or reinstall an old iOS or such, the next thing u need to ask that nobody may have ans for u. has anything automatically happen that can cause this problem. Window is notorious with this, with their automatic update.
Then u have to do basic self daignostic on the system.
Lets say we have a web server and I have problems connecting to this webserver, I can go in and see cpu working appropriately is it under 50percent usage, if I go in and findout that the web server has an 100%
CPU usage all the time. That means the processor is working very hard, I can find out thats the problem. If the webserver isnt something I repair, I maynot go any further. I may find out that the cpu is peg out. Then I call the person who is responsible for the web server and say hey ur web server is at 100%, do u want me to do smthg or do u wanna try something fix it.
Even if u r not the one who is responsible for fixing the problem, u can
find out info that if the person that does come in and whose responsible uk they have a step ahead. U dont just go and say its the web server, go fix it. U say I already looked at it. The cpu is pegging out 100%, these are the things I have seen and he goes from there. Once u done that and u figure out things have changed. U have the basic self diagnostic. Thats where u

go and down very nitty gritty fine tune troubleshooting, thats where u ping stuff and see if device drivers are working properly and u see there is a virus.
Once u seen has anything changed cuz thats most likely to be gonna be the problem, then u gone and done the self test and u seen what the big issue maybe, is the cpu overloaded, then u go down the fine-grain stuffs.looking for viruses or maybe configuration errors and something like that, thats what u do once u get down the computer itself, the device itself.

Reporting (cya)
now this point, we come in the problem situation, we ask around, the overall and all the parts that might be part of the problem and then we troubleshoot large areas and diagnosed specific device on the network, thats causing the problem. At this point, we have done a little bit self diagnostic on the piece of equipement,we have ask is anything is changed.
Either we have fixed the problem or we are not allowed to fix the problem, so we have handed it out to somebody else.
This point of troubleshooting process is the reporting process, now then u have done all this, now that is out of ur hands. Either the problem is fixed or u handed off to somebody, u need to then report to the appropriate people. U need to report to the person that the phone in or told you about the problem. So u know the problem is fixed, yay ok. Or the problem is not fixed but this is the person who’s now responsible for, heres their contact information and this is as far as I understand whats going to happen next.
The person u handed everything off to, should then talk to these people.
Very least u need to do the communication. U need to tell them everything is handed off.
I troubleshoot all this things, this is where I found the problem to be. I am not allowed to fix this problem, tell them why, this is out of my responsibility, I am not trained into that, the guy has taken this on, he said it should be x,y,z. U’ll have to talk to him. U told that to the person who told u about the problem, u tell that to the point of contact. The person who makes the decision, writes the check.

So lets say secretary was having a problem, u fix her probem. Then u just knock on the door to the department manager and say I was fixing this issue, for your secretar, its out of my ability to fix, but we did narrow it down to specific piece of hardware.

The guy is fixing it, he should be along and he’ll tell u whats going on next.
So everybody is in communication, and say ‘eli was working on it and uhh where did eli go and its still not fix, damn eli’
also ‘ u maybe handed to guy and guy is a complete idiot’.
So u tell ppl u handed to guy and when guy does dumb stuff u dont get the blame for it.

Once u reported to anybody, then whether u an employee or the consultant the contractor, then ask them if theres anything else. Just be very polite. So now 2hrs job turn into 8hrs job.

Final part of the troubleshooting process is within reasonable amount of time, callback point of contact and the person who has the problem.

Did u get ur new computer in, is it working kk for u, if I need a new internet connection, it might takes two weeks to get that in. In two weeks call them back and say kk u now on a new internet connection, has that fixed the problem, by doing this u show u just not forget about the people and u may find out ur diagnosis was incorect. Ppl dont mind if u r wrong, ppl dont mind even paying a little money even if u r wrong. Ppl mind u got paid some money and problem isnt fixed and u just disappear in thin air.

So u fix smthg call them in 2,3 days, so u dont put a bandate on problems, where they think the problem was fixed overall, realistic u just put a bandate on it, n 3 days the thing is broken again.

Virtual Private networking

VPN allows computers or entire networks to connect to each other over the internet securely. So if u have an office in seatle and it needs to connect to a office in washington dc securely. Vpn is a client server architecture. Vpn servers and vpn client and the software allows vpn client to securely connect to the vpn servers.

Practical applications in the real world

allows computer and networks to connect to each other securely over the internet.

Virtual private networking

Internet was created for us military for communication, why not telephone were used cuz the communication goes through central hub.
 So if u r in seatle and u wanna contact dc, ur communication goes through central offices in order to go to dc.

The problem is one of the central offices is taken out by nuclear warhead, theres no way to easily re-route this communication
to dc. So if soviet would bomb us and take down few of this central offices, our communication infrastructure would fall apart. So basically military units on the west coast can’t talk to military unit in the east coast.

So what the military wanted, they wanted to a way to communicate that would be self healing, very easily and very quickl. If the central hub was destroyed, the communication would remain online.
With internet all communication is routed with things called router.

the problem with this, from computer security stand point is u have all these routers, these router have data traffic actually have data traffic going through them, so not only is this router moving traffic from it to next router down the line, but all the data is actually going through it, the emails are going through it,files …
so u r hacker, u can collect all the info thats going through and put it back together and see what people are doing, so a man in a middle attack.
Man in middle attack is when 2 ppl are trying to communicate,u get into the middle of that communication stream and u just start reading everything thats going by.
So when internet was created it was for physical security stand point it was very very good, cuz nuclear bomb went off and half of this router are gone, communication still exist.

From data security standpoint, it was very insecure.
So they came up with vpn, vpn allows u to connect to the internet securely.
How it does this, is by using couple of security tools.
1) it uses a tunneling protocol. When its trying to connect to this server in dc. Tunneling protocols sets up a tunnel between u and dc through all the routers u going through. And inside this tunnel it encrypts all of this info. So u created a tunnel aroung the info u sending and then u encrypt all of the info in the tunnel to the people u sending to.
The reason why this is important, cuz if a hacker is sitting on a router and if he is able to see all the traffic thats going through, the first security is going to run into is the tunnel thats protecting ur encrypted data. If they are sophisticated hackers they can penetrate the tunnel, even if they penetrate the tunnel, that data is encrypted.

So if u r trying to connect using vpn, u can connect many of the routers to get to from A to B.
Part of the tunneling protocol: is if a hacker is in middle, if he tries to penetrate this tunnel, this tunnel will try to detect penetration.

If it detects somebody is trying to hack into it. The tunnel will shut himself down and will recreate itself through another set of routers.
Think of it as data tube trying to protect ur data.

Vpn is a client server technology.
There is one server that tries to provide a service and theres a client that connect to this service, so whenever u doodling with a vpn technology. U’ll always have a vpn server. This vpn server will be sitting in ur office, wherever it is u trying to connect to, then u have a vpn client. The vpn client is generally installed on the computer that ur using that will be connected to this office. So if u r using a laptop computer, u may installed or may use a vpn client that is already installed onto that computer.
So what happens, u turn on the vpn client on ur computer or on ur laptop, it’ll say where we trying to connect to. Generally u give it something like an external ip address) where u trying to connect to. U’ll pass ur credentials (username and password). What happens when u connect to the vpn server in the office. Ur connection will go zig-zag to the internet and comes here to the vpn server.
The vpn server will look the credentials and see is this person allowed on the network.
Microsoft,cisco etc have their own vpn software.
Whatever vpn server you using, u have to use vpn client that would work with it.

So if ur in dubai and u connecting to dc, u can use vpn tunnel to connect to ur office in dc, as far as ur computer is concerned, u r actually connected inside this office. So u r now part of the internal network.
So ur computer gonna thing its inside the office, and the computers inside the office gonna think ur computer is inside the office.
Remember u r not in the lan that has speed of 100mb/s
Your speed on ur pc, when u go to the internet, is whatever the speed of the internet connection is.
Let say u have fibre optic conn, ur dc office only has a dsl conn, dsl upload speed is 756kbs. So u r trying to edit a 100Mb files, that files needs to get pushed out at 756kbs connection to u in dubai. The upload speed ur office will affect the user of the vpn.

Old bldg have bad wire, bad wiring is bad for transmiting data.for dsl,cable.

If a hacker is trying to penetrate a tunnel and it will drop the tunnel and recreate it using a new path.

Hacking attack looks like data signal isnt steady, is the data stream gets slow down, if theres too many drop packets. Bad wiring drops a lot of packets and slows things down. Vpn technology things packet loss is hackers trying to penetrate the tunnel. Therefore the vpn keeps dropping the connection and then recreating the connection.

With vpn, active directory,group policy, shared permission.
Ms server have vpn build into their servers and client os.
If u buy windows server, it has routing and remote access build into it.

Alot of this is vendor specific
If u have cisco vpn client, theres a good chance it wont be able to connect to the ms vpn server. If u use open vpn client, u need a open vpn server. If u use cisco vpn server, u need a cisco vpn client.

Voice over IP

Voip servers or ip-pbxes are the main server that route ur calls over voice over phones and devices.

Normal phone system have pbx, so within ur bldg. From this all ur telephone, callboxes, auto attendants goes through pbx.
This is for telephone sys.

When we are talking about VoIP we arent talking about telephones, we are talking about data devices that transmit real-time audio communication, as we go further in this track, this gonna be more and more important.

VoIP server they use tcp/ip ethernet cable, all of your phone the pbx etc is going to use ethernet and its going to use tcp/ip to communicate so instead of having telephone pbx with phones n everything that they’re in their own world. You know have a phone system that resides on the same network as everything else. So u use router, switches, tcp/ip, computers.

U can have ur client telephone connects to VoIP server through the normal network. You can also have analog or digital ports connected to the voice over Ip servers. Some of the voip server, u’ll actually be able to plug a normal telephone straight into it. So lets say you bring in your telephone from home, some of these VoIP servers u can plug that home telephone into the voice over ip servers. It depends on whether they have little plug that allows u to do that.
In VoIP all your communication happen over your normal ethernet network tcp/ip. If they have these little ports on here they can also connec
normal phones but they have got to have those little ports.

Trunk lines
so how do u call in and how do u call out from a voice over ip server.
First way is if u r doing completely voice over ip, u can have a voice over ip trunk from a provider. The company is onsip, there are companies that will provide u ip trunk lines, so u dont need normal telephone lines anymore. You can get all ur calls straight through the internet.

So when u go to call out, ur little phone connects to voip server, the voip server then connects to those voice over ip trunks or on your voice over ip servers u can have connections that connect u to normal phone lines from the outside world. So ur VoIP server replaces the pbx u have before.
B4 u have a special electronic device called pbx that routed all ur telephone communications.

Now u have a VoIP server, all ur VoIP devices connects to it. It is the one that route calls to the outside world.

Now we are doing everything over ip, now we are doing everything over ethernet network this VoIP server nolonger has to be in our bldg.
So u can have ur VoIP server hosted on the outside world.
Just like u have a email server out on the internet, u can have the VoIP server out here, and basically u rent this from a company, lets say company like onSip or other ones, they’ll host ur VoIP servers for u.

So u have all ur telephones in the bldg all ur computers, telephones etc, they connect to the switch, the switch connects to the router and then they all connect to this voice over ip server thats no longer even in ur bldg.
Why because everything now uses tcp/ip and the ethernet networking standard.
Good thing, cuz whether they are normal pbx or VoIp service cost a lot of money, for a basic voip server that u going to put into a businees its going to cost 2000 $ just for the server and then u add your phone lines that you have to pay for and add in all this other stuff and it gets to be very expensive and now that u can pay for a simple voice over ip service. You just pay 25 or 50 or whatever/ month per phone and u dont have to worry about the box sitting inside ur bldg.
U get the whole enterprise class functionality, all the phonelines and everything, it all works but its all now out on the internet. U dont have to buy the box for the voip server.
These voice over ip server can be manufactured by normal companies, companies u probably heard of aviva, luscent, at&t, nortel, mytel etc. Those our proprietary voip servers or ip pbxes. Or they have new companies out such as astras,sipx, these are free open source VoIP servers that can basically uk how to install them and setup a computer, u can have a completely free enterprise class VoIP servers for the cost of a computer that was on the corner collecting dust.
These voice over ip server, they act like the pbx we talked about, they route all the communications, they contain the auto attendance, they contain the call tree, call pads, huntgroups etc.

so they do the normal routing that the old pbxes did, the difference is they communicate using ethernet tcp/ip vs the old phone line. The old pbxs did.

Voip clients
Voip server, this is a computer that provides services to other computer on the network. All ur devices or clients going to connect to this voice over ip server. Whether its a telephone or its a computer,etc.

Hardphones and softphones:
hardphone is a computer device that looks like telephone its grey and have a handset.
Its an actual device all it does, provide telephone service or real time audio communication service. If u look at VoIP telephone it looks like a telephone.
Softphones is a piece of software that installed onto a computer to allow that computer to provide real time audio communication.
Any of the computing devices, that normally considered a phone, and u installed a piece of software onto it, then its a softphone.
Softphone are software that allow computer devices to act as phones.

You configured hardphone using web interface. You would go to the ip address for that phone, when u open it up, theres a little web browser. That little thing is actual a web server. You would configured everything through the web server that reside on that hardphone.
These devices connects to account within voip server, so in the voip server u setup the user account.

In the voIp server u setting up extension 105 and have user:x and pwd:y.
And ull set whole bunch of other config. These are most important cuz
in VoIP client u go to the client whether its the ipad, pc, hardphone.
Inside even the hardphone, u say this phone is extension 105, wid username of x and pwd of y.

with old pbx, everthing was configured inside the pbx itself, with the voip server, uk have a client server connection. So u create a user account within the voip server and for the device thats connecting, u need to give the information for it to provide voip server.

So u pass the credentials, and when this phone gets on the network, it’ll connect to the VoIP server and it’ll say my username is x and my pwd is y.
I want extension 105.
the voip server say will authenticate and say u r now extension 105.
so if somebody calls in from the outside world, they dial extension 105, they will now go to this phone.
Softphones are pieces of software that u installed on normal looking computers. To make them act like a phone. So if u have a normal computer , laptop computer, netbook computer , ipad. U would install softphone onto it, that allows that computer to connect to VoIP server and allows that computer to act like a telephone.

VoIP gateways.
Gateways are what connect different types of communication network. In old days, all they did is turn voip connections into normal telephone calls.
So what would happen, is u have ur voice over ip server and lets say u r on the internal network and u make a call from one phone to another.
It was all VoIP. So I make a call it goes through voip server and route to that phone.
So if bobs in a house, he has a normal phone, he doesnt have VoIP phone. So what they did is created something called gatway, so in gateway, if u r trying to call outside line what they did, they have nomral Rj11 telephone connector, so u can connect normal telephone line from the outside world into this gateways. So the telephone lines u have in ur house, u can connect to one of this gateways. So that gateway is connected to normal telephone line and then u can call into bob house.
 So basically what would happen, so if u call from ur voice over ip phone, that would get routed to VoIP server and that call would get routed to a gatewayand that gateway will send the call out to the
normal telephone lines.
So this gateway connected to normal VoIp world and telephone world.

Enterprise companies have lots and lots of offices, u have ur offices all over everywhere. They already had to pay for internet conn, t1 conn to all of the remote offices regardless.
So if u have a billing department, so what we did is created lots of residential customer.
Imagine our installaton department was 20 miles from customer, but our billing department was all the way in middle of america. So our billing department wants to call this customer, it will be a long distance charge.
Again if u dealing with one and 2 ppl this isnt a big deal, but when the billing department is 100 ppl, thats a whole bunch of money.
So in our central office we gonan have a VoIP phones, so we gonna have phones that use our internet connection, and in the remote office we gonna put a gateway that allows us to call local numbers. So what would happen wid VoIp traffic, it will be send through over t1 line down to voip server and it will get routed to this gateway and from this gateway its a local telephone call to that client.
Now, gateways specially design that skype voip traffic can now be turn into normal sip voip traffic.
So if ur company or company u use is already using skype phone no, u can have a skype gateway that will connect u to a sip voip sys. These gateways connect diff types of communication networks basically.

VoIP protocols

Session initiated protocol is a ratified protocols tha lots of companies use, u can buy cisco sip phones. U can buy polycon sip phones, astras..
Sip reside on top of tcp/ip, this a application layer networking communication, this can ride on tcp/ip or udp. Some of the major manufacturer they really dont like open source.

VoIp codecs
this is how voice traffic is actually encoded and encapsulated, so when ur talking into the phone, ur communication has to be put into a little packets and send down the network and ur codec determines how this happens.so if u want really high quality Voip traffic and u have a lot of bandwidth,u’ll use codecs.
So lets say u r on crappy network, u dont have a lot of bandwidth on the network, ur codec is was what would determine, lets say I wanna use lesser great codec, where our communication isnt gonna send as good, but will use less bandwidth. Every voip server will have codec built into it.
When u buy voip server they’ll give u license to use proprietary codecs or they’ll give u open source codecs.
The sound quality maybe fine, but the bandwidth will be bad.

Network latency and Qos

is when somebody starts talking, how long does it take those bits to go from u to the voip server.
45ms:avg
75-100ms:ok in voip

Unified communication:
 so u could have a softphone like ur laptop so why not have a outlook plugin, so u can make a call straight from the plugin.

Open dns:

if u compromise dns server u can compromise to whatever website u want them to go to.
In open dns, some url is passed, open dns will redirect it to ip address of open dns server, which will say u r blocked u cant go to any website.
So if ppl on ur network r trying to go to bad site, u can prevent them from going. So when their computer tries go to the ip address of the domain name, the ip address they’ll get will be a incorrect one. It will send them to open dns server.
The reason dns is so poweful as a security process, cuz this is not simply ur web browser blocking certain site, its not that firefox blocks u to a website or u have some filter in IE or chrome. This works at network layer of OSI model.
Even if u did a ping, it will return a different ip address.

Phoning home: once ur computers are infected with viruses it then tries to go out and communicate with servers on the internet to pull in more viruses. These viruses use domain name.

How it works:
There are two places where domain name mapping happens.
1. host file
<ip address> <domain name>
…
…
In the ip config, it will have a primary and secondary dns server, those ip address state if u cant find a domain name in the host file then go to this dns server to try to resolve the domain name.
If u cant find the domain name in the 1st dns then goto 2nd dns to resolve the domain name.
What u can do is change the dns server that your computer goes to so instead of going to the normal public dns server that u would normally go to open dns server and the open dns server will look at ur computer account or network account and depending on what ur network account is set up for it will either allow u or not allow u to go to different domains.

 In ur router, u put in their primary and secondary server.

So what happne when ur computer ask for an ip address from a dhcp server, it will be given the ip address, subnet mask, default gateway and this domains name server.
What open dns does, is in the control panel, u can go to a little website, open up the control panel on the website and u plug in what ur external ip address is, is ur ip address before the internet so. So u plug that in open dns control panel.
So what happens is when u go to open dns, open dns is gonna read what ip address u came from, it will find the account security that corresponds with the ip address u came from and then it’ll give u dns accordingly.
If u dont have static ip address from ur isp.
Install dynamic ip address application from opne dns what that does is when u install it on your computer every once in a while, it will tell open dns what ur current external ip address is, so when u go and u see the open dns server they know what account u’re dealing with.
Put that application on a computer thats always on 24x7, so if ur computer is turned off, n ur isp changes ur dynamic ip addresses, so when u go to the open dns server they wont know who u r, ur security policies wont work.

Dhcp: server-service

dhcp will provide certain pieces of tcp/ip information.
1.ip address, subnet mask, default gateway , primary and secondary dns.
Dynamic:ip address.
Static: subnet-mask, defualt gateway, primary and secondary dns.

Scope:range
Reservation:static
some dhcp server u can say that this ip address Is already taken by server or device on a network.
192.168.1.11: access point
since, this dhcp server have finite amount of ip addresses that theycan give out, what is one of the way to make sure it doesnt run out of ip address.

Because computer come on a network and take ip address and leave the network and the dhcp server doesnt realize it.
SO use a lease, if one day thats how long the dhcp server will reserve the ip address for clients computer.
When a computer is connected to the network, it broadcast a dhcp discover signal on the LAN. Then the dhcp server does dhcp offer and client says kk and dhcp server gives an acknowledgement.

DNS:
in order for home networks to work properly they have dynamic dns setup,
so when a dhcp server when it gives a ip address to a clients computer, its actually doing two things, one its giving ip address to client computer, two its telling dns server what the ip address of that client computer is. So dynamic dns is dhcp dynamically writing to the dns tables to map those host name or domain name to ip addresses.

If that wasnt the case,
the dhcp server will continiously give out ip addresses but that information will not be recorded on the dns server, if u try to ping pc2 and dynamic dns hasnt been setup that wont be able to work because within the dns server that information has not been written.
So Configure the dynamic dns properly.

Reverse DNS:
In normal dns, u map the domain name to ip address, but u dont verify the ip address is the ip address it should be.
In reverse Dns, it maps the ip address to the domain name. So if ur computer is supposed to go to lets say a server in an enterprise enviorment, so it will go to the dns it will make sure that server is supposed to go to …. but then it will also do a query what is 192. . . ? supposed to be. If u had reverse dns setup it will say 192. . . . is supposed to be a server.

---

 so first attempt is gonna look at ur dns server and see in records if he knows which ip address corresponds to this ip address. The dns server will have a primary dns and secondary dns.
If it cant find it here, it will go and look in primary dns.
Extra:-
Amax,cname,a records

software defined networking:
the idea is to pulling away the intelligence from the hardware.
In old days, if we wanna store data, we have file server that had hard-drive that store data most likely in raid configuration. So one box contain hard-drive, data, os , access control list . If anything happen to that drive, everything was unusable. If power supply died, the data storage device was unusable.
SAN: storage area network.
All of sudden the physical storage was seperated from the control mechanism that controls how the data was stored. So in san, u basically have dumbish data storage devices and then some kind of management system that controls where that data goes to.

So with virtualization, all these instances of operating system can flow from different pieces of hardware and as far as operating system is concerned, it doesnt care where its at.

With sdn, we are doing what we have done to data storage and computers, we are pulling the intelligence off of the hardware. We are making a network equipment dumber, but we creating a management system to make the overall networking system, much more intelligent.

So we have a very nuance control of our entire networking infrastructure at one control panel vs having to go in inidividual little router and switches and do different types of changes.

Latency: is how fast can we move individual packets from point a to c.
Qos: prioritize the packets.
So Voip has higher priority than video downloading
before we could say ftp is lower priority than sip.
But as more and more devices connected to the network, its coming to a point sometimes, ftp traffic are higher priority than sip. And sometimes video traffic is more important than voice traffic. And sometimes opp.
The problem is, wid Qos u cant programme like that. U cant dynamically configure like this.

With sdn, we can dynamically model and shape our traffic depending on what we need to do. The big thing is we seperate networking into control plane and data plane. The data plane has all the switches and router that allows packet to go from point a to point b.
control plane is a set of management servers that communicate with all of different networking equipment on the data plane and say right at this sec, how should data move from the data plane. So u can say right at this sec, all sip traffic should have a priority over ftp packet. And 2min from now, all snmp traffic should have higher priority than sip traffic. From the control console, u r able to control the entire network at one place.

SDN:
IS we seperating out different components of the networking infrastructure, so that we can deal with them seperately. So the data plane /section , is how we move data from point a to point b. so we are dealing wid router, switches and so forth.
Service plane: are things like firewall, how many services are there on the network and can u seperate them from the physical equipment.
So if u r dealing with firewall, that firewall software is sitting on a physical piece of firewall hardware, the question is “hey can we have a piece of firewall hardware but then seperate the service the actual firewall functioinality off to a different server so it can deal with it more efficiently, then u have what is called a control plane, the control plane is the server that do all the management for the services and the data and then u have something called the management plane and that is what controls and make sure all the servers on the control plane function as they are supposed to.
The idea behind software defined networking is we are seperating all this out because right now again if u deal with a router u have a hardware and the intelligence and the programming all on that one device. Well what if we can seperate the router hardware from the router intelligence from the router programming then if we do this it allows us to manage our system much more easily.

 SDN allow us to shape traffic in real time. So what if we go out and buy really big powerful networking hardware why would be shaping traffic in real time.

Well whats the point of this?

 whenever u setup a network in real world, everything in real world has its own boundaries, boxes, so we create a voip network, voip has only so much bandwidth, right beside it we would create a digital survillance network and it will have so much bandwidth, right beside it we create a server and computer network and it has so much bandwidth, maybe the bandwidth will be limited by Qos, Vlans.
We setup this network and every single type of service has a limited amount of bandwidth thats allocated to it. Sometimes it uses all that bandwidth and sometimes it uses a very little portion of it.
Sometimes a voip network is using 75% of allocated bandwidth other time, its only using one percent, if u set this with vlans and other things, u may not be able to use all that bandwidth thats not currently being used by voip sys. So it would be nice if we have infrastructure that created again where real time we can prioritize traffic, so we can simply have 1Gb/s pipe and instead of sectioning off to all this different services, we could say we have an entire pipe that is allocated to us, all the time and depending upon on our current needs, different services are running over that network will receive different priority, again eli I dont see why this would be imp?

We are in technology, we have to think 3yrs from now.
As we know being able to sent HD videos take a lot of bandwidth,
ex:-
in workplace voilence,
imagine u r working with 1000 employees (1000 diff workstation), now imagine some pissed off spouse walked in with a hand gun, and say I wanna know where my wife is?
Its best the employee are able to get out off the bldg, tryin to avoid the crazy person, imagine if u have a video alert sys, as the person walks in the bldg.

You can actually stream from ur survillance sys to every single device on the network, the current loc of the intruder and HD video of what he is doing at this sec.
This will take tremendous amount of bandwidth, so If u have a network that is configured as modern networks are, basically it wouldnt work. Because of Qos, vision of the network. So to show HD video to 1000 different workstation.
So if u have SDN, in one instance , u can turn ur entire network over to stream that video to all the computers on the network. So u could press a button or programmelly, voip shuts down, smtp shut down,ftp shutoff,smb shuttoff,
so any protocols thats not with that video stream gets shutoff, so the video stream has the prioritization so it can go out to all those computer.
Police capture that crazy person.
And with sdn, u can turn off the video stream and u can give priority to all the VoIP traffic so all the employees and their loved ones can tell them that they are ok, thats what sdn allows u do, it allows u to allocate and shape traffic depending upon your current needs and that super cool.

The idea behind all this is u are going to be seperating out the networking components to different planes so u have ur data plane which contains all the hardware and the basic mechanisms for being able to forward data from point a to point b. then u have the services plane now why this is important, think about firewalls couldnt they work more efficiently if u can cluster them or if u can use the power of Zeon servers in order to all of the firewall stuff that u want , instead of having a firewall, instead of all the cpu and processing being on the firewall. Imagine u have the power of cloud and u can cluster 10Xeon servers to be to deal with firewall service, wouldnt u be able to do more powerful things and have packets be ablt to be processed much more quickly. The control plane is the management console so u can sit there and u can have one interface that allows u to automatically configure all of the networking equipment on the network, so instead of having to go to this switch and that switch, this router and that router in order to change Qos for a specific protocol, u can simply say I want protocol 25 and to have maximum priority now.
The management plane u manages the control plane because the control plane you can now do things like have servers that control all the networking equipment, u can have clusters of server much like u can have cluster of active directory servers.
Final part when dealing with sdn is “Open flow”
so there’s a control protocol for how u control all this networking devices. So the question becomes, u have the control plane, that controls networking devices but you have to actually communicate with those networking devices right just like u have routing protocols just like u have rip or open shortest path first like that well if u’r going to be using a control plane to be able to talk to the data equipment, u are also gonna need a protocol to deal with that, that is called the control protocol and thats one of the things thats called open flow

the concept is u seperate the intelligence from the hardware you seperate the services from the hardware the hardware the router the switches the bridges, the wap becomes much more dumb and then the control plane controls all of those networking devices. So just like windows 2008 server can controls windows 8 computer on the network so from one interface, u can control all these things.